## Slide 1
CHAPTER 1 | LECTURE | 45 MINUTES
Why a Game, Why RISC-V, Why Now
The case for learning architecture and programming by building retro games on an open processor
Audience: first-year computer architecture and programming students
Playing with RISC-V: Assembly, C, and Retro Games on the PRG32 Platform
Notes: Teaching support for Chapter 1 of the textbook. Front lecture: about 45 minutes including the questions.

## Slide 2: Learning objectives
1
Explain why a game is a rigorous teaching object, not a gimmick
2
Define an instruction set architecture and say what makes RISC-V open
3
Summarise why Europe treats RISC-V as strategic
4
Describe PRG32 and its ecosystem in a few sentences
5
Choose the track of the book that matches your course
Notes: State the objectives; return to this slide at the end.

## Slide 3: Agenda
7'
8'
12'
7'
11'
1
The problem: two courses, two universes
2
The platform in one paragraph
3
RISC-V as strategic European IP
4
Why retro games
5
The ecosystem and the book
Notes: Total: 45 minutes.

## Slide 4
On Monday you traced addi by hand. On Thursday you ran a C program. Was it the same machine?
Most first-year students cannot say yes with conviction. This course exists to make the answer obvious.

## Slide 5: The problem this course solves
1
Computer architecture shows the bare machine, but the reward is often a number on a terminal
2
Programming gives power through abstraction, but the machine disappears from view
3
Students pass both and still do not connect an instruction with a running program
4
We need one object that both courses can look at, at two altitudes

## Slide 6: Two courses, two universes
Computer Architecture
Registers, instructions, memory
Precise, but feedback is thin
Language: RISC-V assembly
Risk: 'why does this matter?'
Computer Programming
Variables, functions, structures
Productive, but the CPU is hidden
Language: C
Risk: 'the computer is magic'

## Slide 7
When a rectangle slides left because you set one bit, the distance between instruction and consequence collapses.
The screen is honest in a way a grade is not.

## Slide 8
01
The platform in one paragraph
PRG32: an open educational runtime for RISC-V assembly and C games

## Slide 9: PRG32 in four facts
1
Native code
Your program runs as 32-bit RISC-V machine code. PRG32's reference targets do not interpret it.
2
Two reference targets
A physical ESP32-C6 board, and Espressif QEMU on your laptop. Same source for both.
3
Cartridges
A game is a small .prg32 file that the resident firmware loads and runs. No reflashing.
4
Three functions
init once; update and draw once per frame. Identical in assembly and in C.

## Slide 10: The whole contract between you and the machine
init
runs once
read input
buttons, time
update
change state
draw
render state
After init, the runtime calls update and draw once per frame, forever. Every example in the book, in either language, has exactly this shape.

## Slide 11: A complete game is a handful of rectangles
ball
paddle
(0,0)
320 x 200 game viewport
1
Viewport 320 by 200 pixels, 16-bit colour
2
Small enough to hold the whole program in your head
3
Rich enough for state, input, arithmetic, branches, a loop

## Slide 12: Deliberately thin, so the processor stays in view
1
No engine, no scene graph, no garbage collector between you and the CPU
2
A complete Pong cartridge is about 3 KiB of code
3
Every register and every byte of state can be inspected
4
Constraints are the pedagogy: tight memory forces understanding
3 KiB
a complete Pong cartridge, inside a 64 KiB budget

## Slide 13: The machine in numbers
Quantity | Value
Processor | ESP32-C6, RV32IMAC, 160 MHz
Main RAM (HP SRAM) | 512 KB at 0x40800000
Game viewport | 320 x 200 = 64,000 pixels, one byte each
Frame period | 33 ms: about 30 frames per second
Audio | 8 voices, 22,050 Hz, I2S
Cartridge RAM | 64 KiB by default; 4 flash slots
Runtime interface | 139 functions, ABI 1.6
Notes: Sources: PRG32 docs/hardware/memory.md, prg32.h, prg32_abi.json.

## Slide 14: What 160 MHz buys per frame
1
33 ms at 160 MHz is about 5 million clock cycles per frame
2
Clearing the screen touches 64,000 bytes
3
A Pong update is a few hundred instructions
4
The budget is generous for logic and tight for pixels: draw less, not faster
5 M
cycles per frame

## Slide 15
02
RISC-V as strategic European IP
Why this processor, and why the choice reaches beyond the classroom

## Slide 16: What an instruction set architecture is
1
The contract that defines what a processor's instructions mean
2
The deepest layer at which a region can be technologically independent
3
For decades the dominant ISAs were proprietary and licensed
4
RISC-V is an open standard: anyone may build a processor without an architecture licence fee
Notes: RISC-V is pronounced risk-five: the fifth generation of RISC research at UC Berkeley.

## Slide 17: Proprietary versus open instruction sets
Proprietary ISA
Owned by one company
Licence required to build a CPU
Roadmap decided elsewhere
Extensions by permission
RISC-V
Shared, open specification
No architecture licence fee
Governed as a standard
Extensions by design

## Slide 18: The European numbers
Indicator | Value | Source
Global semiconductor market | about 700 billion USD | HiPEAC 2026
Europe's current share | about one tenth | HiPEAC 2026
European Chips Act target | one fifth by 2030 | Chips Act 2023
DARE project funding | about 240 million EUR | EuroHPC JU
Notes: Orders of magnitude, as cited in the textbook; check the sources for current figures.

## Slide 19: Programmes built on RISC-V
1
European Chips Act
Sets the goal of doubling Europe's share of the semiconductor market.
2
DARE
Digital Autonomy with RISC-V in Europe: processors and accelerators for HPC and AI.
3
European Processor Initiative
The earlier programme whose lineage DARE continues.
4
TRISTAN
Chips JU project assembling verified, industry-ready RISC-V IP.
Notes: The recurring word in all of these announcements is sovereignty.

## Slide 20: What transfers from this course
1
addi, lw, sw, beqz are not a teaching dialect
2
They are the instructions European industry is building processors on
3
The calling convention you learn is the real RV32 convention
4
Reading RISC-V is a foundational skill and a small act of participation

## Slide 21: Check your understanding
What makes RISC-V 'open'?
A
Its processors are free of charge
B
The instruction set specification can be implemented without an architecture licence
C
All RISC-V chip designs are open source
D
It only runs open-source software
Notes: Answer: B. Openness concerns the ISA specification. Individual chip designs may be open or proprietary.

## Slide 22
03
Why retro games
Which kind of program teaches the most per line?

## Slide 23: The pedagogical sweet spot
1
Small
A beginner can hold the whole program in mind at once.
2
Complete
State, input, arithmetic, decisions, and a timed loop: every first-course concept.
3
Honest
A wrong sort may print plausible numbers. A wrong game puts the ball through the paddle.
4
Constrained
A tight budget and a simple display force you to know what is happening.

## Slide 24: What Ready Player One understood
1
Foundational layers do not become obsolete; they become invisible
2
Those who can still see them keep a kind of power
3
Drawing a sprite pixel by pixel is the substrate of every modern abstraction
4
Retro development preserves and transmits that literacy
Notes: Cline (2011). Use the novel as a cultural hook, not as an authority.

## Slide 25
04
The ecosystem and the book
One runtime, four projects, three tracks

## Slide 26: How the pieces fit
Construction Kit
blocks to C
Assembly or C
hand-written
prg32 tooling
.prg32 cartridge
Cartridge Store
review, catalogue
Board, QEMU, PRG32-QT
hosts
Every path ends in the same portable cartridge, and every host runs it.

## Slide 27: The PRG32 ecosystem
Project | Role | In the book
PRG32 | Firmware, cartridge ABI, python3 -m prg32 tooling, examples | Everywhere
Cartridge Store | Catalogue with editorial review; scores, metrics, multiplayer | Chapter 17
Construction Kit | Blocks editor, simulator, sprite editor, C generator | Part IV
PRG32-QT | Portable host for desktop, mobile, TV, with a debugger | Chapter 4

## Slide 28: Three ways to run one cartridge
 | ESP32-C6 board | Espressif QEMU | PRG32-QT
Execution | Native | Native on emulated C3 | Interpreted RV32IMAC
Needs ESP-IDF | Yes | Yes | No
Best for | Real timing, real feel | Real firmware, no hardware | Stepping and inspecting

## Slide 29: How the book is arranged
1
Part I: foundations, for everyone
2
Part II: the Computer Architecture track, in RISC-V assembly
3
Part III: the Computer Programming track, in C
4
Part IV: the Young Makers track, in blocks, with a chapter for teachers
5
Part V: assembly meets C, and publishing on the Cartridge Store

## Slide 30: Check your understanding
Which statement about PRG32's reference targets is true?
A
Game code is interpreted by a virtual machine on the board
B
Assembly and C games use different runtime interfaces
C
The same source builds for the board and for QEMU
D
A cartridge must be flashed together with the firmware
Notes: Answer: C. Same source, two targets. Cartridges are loaded by the resident firmware without reflashing.

## Slide 31: What to take away
1
A game gives immediate, honest feedback on low-level code
2
RISC-V is an open ISA and a European strategic choice
3
PRG32 is thin by design: three functions, native code, small cartridges
4
The same cartridge runs on a board, on QEMU, and in PRG32-QT
5
Pick your track; the foundations and the publishing chapter are shared

## Slide 32: Next steps and reading
Before the next session
Read Chapter 2: the frame loop and the framework
Skim the PRG32 README on GitHub
Install PRG32-QT and play one Store cartridge
Write three sentences: why RISC-V?
Reading and sources
Textbook, Chapter 1 and the Preface
PRG32 repository: github.com/riscv-prg32/PRG32
RISC-V International, the RISC-V ISA specifications
HiPEAC (2026) and EuroHPC JU on DARE
E. Cline, Ready Player One (2011)