## Slide 1
CHAPTER 3 | LABORATORY | 45 MINUTES
Setup Lab: From Empty Shell to Running Cartridge
A reproducible walk from an activated toolchain to a cartridge you wrote, built, inspected and ran
Audience: first-year computer architecture and programming students
Playing with RISC-V: Assembly, C, and Retro Games on the PRG32 Platform
Notes: Teaching support for Chapter 3 of the textbook. Practical, step-by-step session: learners work at their machines; keep each step to its time box. Preparation: ESP-IDF 5.4 installed beforehand (20-40 minutes). The textbook repository cloned next to PRG32. Reference files: labs/03-setup/step1..3.

## Slide 2: Learning objectives
1
Activate ESP-IDF and verify it with doctor
2
Build and start the QEMU firmware
3
Write, build, inspect and run a cartridge in three steps
4
Read the build log and the cartridge summary
5
Recognise the failure caused by an unsaved return address
Notes: State the objectives; return to this slide at the end.

## Slide 3: Plan of the session
8'
9'
16'
5'
7'
1
Verify the environment
2
Emulator firmware
3
Hello world in three steps
4
Inspect
5
Break it on purpose
Notes: Total: 45 minutes.

## Slide 4: Rules of the bench
1
Type the commands; read every line of output
2
When something fails, read the FIRST error
3
Each step ends with something you can see
4
Write down every number the tools print

## Slide 5
01
Verify the environment
Nothing else works until this does

## Slide 6: Activate ESP-IDF
1
Open a new terminal (Windows: the ESP-IDF PowerShell)
2
. $HOME/esp-idf/export.sh
3
idf.py --version
4
riscv32-esp-elf-gcc --version
Step 1
about 3 min
Expected result
ESP-IDF v5.4 or newer, and a GCC whose target is riscv32-esp-elf.

## Slide 7: Get PRG32 and run the doctor
1
git clone https://github.com/riscv-prg32/PRG32 && cd PRG32
2
pip install pyaudio zeroconf
3
export PRG32_HOME=$PWD
4
python3 -m prg32 doctor
Step 2
about 5 min
Expected result
Four [OK] lines, as on the next slide. Any [FAIL] means ESP-IDF is not active in this shell.

## Slide 8: What doctor prints
[OK] idf.py found
[OK] riscv32-esp-elf-gcc found
[OK] partitions file found: ~/PRG32/profiles/partitions_prg32.csv
[OK] partition cart0 parsed (offset=0x210000, size=131072)
1
The build system
2
The RISC-V cross-compiler
3
The flash layout
4
Slot cart0: 131072 bytes = 128 KiB of flash
Notes: Output captured from a real run.

## Slide 9: Check your understanding
doctor reports that riscv32-esp-elf-gcc is missing. Most likely?
A
The repository is corrupted
B
ESP-IDF is not active in this shell
C
QEMU is not installed
D
The cartridge is too large
Notes: Answer: B. Source export.sh again.

## Slide 10
02
Emulator firmware
The real firmware on an emulated chip

## Slide 11: Build and start QEMU
1
python3 -m prg32 qemu build
2
python3 -m prg32 qemu run
3
Click the TERMINAL, then press the arrow keys
4
Find Run Cartridge in the setup menu; press X to go back
Step 3
about 9 min
Expected result
A build-qemu directory with qemu_flash.bin, then a window with the PRG32 screen. The terminal logs 'prg32_main: PRG32 runtime initialized'. Keys work only while the terminal has focus.
Notes: The first build takes several minutes: use the time for the next two slides.

## Slide 12: If the QEMU build stops at esp_crt_bundle.h
1
Seen on PRG32 main (a8669e5) with ESP-IDF v5.4, when building from a fresh clone
2
Error: prg32_store.c: fatal error: esp_crt_bundle.h: No such file or directory
3
Cause: the prg32 component does not list mbedtls for the QEMU target
4
Fix: in components/prg32/CMakeLists.txt add the line 'mbedtls' after 'spi_flash' in PRG32_PRIV_REQUIRES
5
Run the build again; it continues from where it stopped
Notes: Verified while preparing this lab: with that one line the build completes and QEMU boots. Remove this slide once the fix is upstream.

## Slide 13: Keys in QEMU
PRG32 control | Key
Joystick | Arrow keys or W A S D
A (confirm) | Z or J
B (back) | X or K
Start / Select | Enter or Space
Notes: QEMU reads the keyboard from the terminal that launched it, not from the screen window.

## Slide 14: How every step works
1
Each step is a complete file in labs/: read what is new, then run it
2
From the textbook folder: labs/run.sh STEP_FILE PREFIX builds and starts it
3
Set PRG32_HOME to your PRG32 checkout; set PRG32_URL to run on a board or PRG32-QT, otherwise QEMU starts
4
The screenshot on each slide is that exact file, built and executed
5
After each step: change one thing, predict, run

## Slide 15
03
Hello world in three steps
Skeleton, text, more text

## Slide 16: Step 1: the skeleton
# Setup lab: the first cartridge, from an empty file.
.option norelax
.section .text
.global hello_world_init
.global hello_world_update
.global hello_world_draw
hello_world_init:
ret
hello_world_update:
ret
hello_world_draw:
ret
1
.global exports the three entry points
2
Each function returns at once
3
This is already a valid cartridge
Notes: Source: labs/03-setup/step1_skeleton.S

## Slide 17: Build it by hand, once
1
mkdir -p work/hello && cp ../Playing-with-RISC-V_PRG32_textbook/labs/03-setup/step1_skeleton.S work/hello/hello.S
2
python3 -m prg32 cartridge build work/hello/hello.S --portable --entry-prefix hello_world --name hello --out work/hello/hello.prg32
3
python3 -m prg32 qemu upload work/hello/hello.prg32 && python3 -m prg32 qemu run
Step 4 | about 5 min
Expected result
[OK] built ... code=2604 mem=2604, then a black screen: the runtime is calling three functions that return.
Notes: Adjust the copy path to where the textbook repository is. Close QEMU before every upload. Screenshot: this step, built and run: labs/03-setup/expected/step1_skeleton.png

## Slide 18: Reading the build log
[INFO] Portable: True
[INFO] Building cartridge: work/hello/hello (Prefix: hello_world)
[INFO] Cartridge RAM limit: 65536 bytes (default firmware profile)
[OK] built work/hello/hello.prg32 name=hello load=0x40800000
[INFO] code=2664 mem=2664 audio=0
1
Portable: calls go through the ABI table
2
The limit of the 64 KiB profile
3
Load address of every cartridge
4
Sizes in bytes (this is step 2)
Notes: Output captured from a real build of step 2.

## Slide 19: Why an empty cartridge is 2604 bytes
1
Your three functions are 3 instructions
2
The builder adds one small stub per runtime function: 139 of them
3
Each stub loads the ABI table and jumps to its entry
4
Plus three entry trampolines that save the table pointer
5
So every cartridge starts at about 2.6 KiB
2604
bytes: stubs and trampolines

## Slide 20: Step 2: text on the screen
hello_world_draw:
addi sp, sp, -16
sw ra, 12(sp) # this function calls others: save
ra
li a0, BLACK
call prg32_gfx_clear
li a0, 32 # x
li a1, 40 # y
la a2, title # address of the string
li a3, CYAN # foreground colour
li a4, BLACK # background colour
call prg32_gfx_text8
lw ra, 12(sp)
Screenshot: this step, built and run
draw now calls two functions, so it saves ra. Five arguments in a0..a4: x, y, string address, foreground, background.
Notes: Source: labs/03-setup/step2_text.S

## Slide 21: Run step 2
1
labs/run.sh 03-setup/step2_text.S hello_world
2
Copy the new lines into your work/hello/hello.S and build it yourself
3
Change x and y of the text
4
Change CYAN to 0xF800
Step 5 | about 6 min
Expected result
HELLO WORLD in cyan at (32, 40); then where and in the colour you chose. code=2664: 60 bytes more than the skeleton.
Notes: Screenshot: this step, built and run: labs/03-setup/expected/step2_text.png

## Slide 22: Step 3: a second line
call prg32_gfx_text8
li a0, 32
li a1, 64 # 24 pixels lower
la a2, line2
li a3, WHITE
li a4, BLACK
call prg32_gfx_text8
Screenshot: this step, built and run
The same five-argument pattern again, 24 pixels lower, with a second string in .rodata.
Notes: Source: labs/03-setup/step3_two_lines.S

## Slide 23: Run step 3
1
labs/run.sh 03-setup/step3_two_lines.S hello_world
2
Add a third line of your own at y = 88
3
Give it a colour you computed in RGB565
Step 6 | about 5 min
Expected result
Two lines, then three. Each extra call costs about 60 bytes: check code= in the log.
Notes: Screenshot: this step, built and run: labs/03-setup/expected/step3_two_lines.png

## Slide 24
04
Inspect
What the firmware will read

## Slide 25: Read the summary
1
python3 -m prg32 cartridge summary work/hello/hello.prg32
2
Find header_size, code_size, mem_size
3
Find import_model and abi_hash
4
Convert load_addr 1082130432 to hexadecimal
Step 7
about 5 min
Expected result
header_size 100, code_size about 2724, import_model "abi-table", abi_hash "0x260f6136", flags 4. 1082130432 = 0x40800000.

## Slide 26: The summary, field by field
Field | Value here | Meaning
header_size | 100 | bytes before the code
code_size / mem_size | 2724 / 2724 | code+data, and with .bss
import_model | abi-table | portable cartridge
abi_hash | 0x260f6136 | the table it was built for
flags | 4 | bit 2: uses the ABI table
load_addr | 0x40800000 | start of cartridge RAM
Notes: Values from a real build of step 3.

## Slide 27
05
Break it on purpose
Learn the symptom while you know the cause

## Slide 28: The unsaved return address
1
In your hello.S delete 'sw ra, 12(sp)' and 'lw ra, 12(sp)' in draw
2
Predict what happens at draw's ret
3
Build and run
4
Restore the two lines
Step 8
about 5 min
Expected result
The cartridge never finishes a frame: draw returns into itself. QEMU freezes; PRG32-QT stops it and reports 'instruction budget exhausted'.
Notes: Verified: the headless PRG32-QT runner prints 'frame 0: instruction budget exhausted'.

## Slide 29: Check your understanding
Why does draw return into itself?
A
The stack overflowed
B
call overwrote ra with an address inside draw, and ret jumps to ra
C
The string was too long
D
QEMU has a bug
Notes: Answer: B. The original return address was never saved, so it was lost at the first call.

## Slide 30: You can now
1
Verify a toolchain with doctor
2
Build, upload and run a cartridge by hand
3
Read the build log and the summary
4
Explain why the smallest cartridge is 2.6 KiB
5
Recognise an unsaved ra by its symptom

## Slide 31: Next steps and reading
Before the next session
Keep work/hello: it is your scratch cartridge
Install PRG32-QT for the next lab
Assembly track: Chapter 5. C track: Chapter 9
Reading and sources
Textbook, Chapter 3
labs/03-setup/ in the textbook repository
PRG32 docs/usage/getting_started.md and troubleshooting.md