## Slide 1
CHAPTER 4 | LABORATORY | 45 MINUTES
Debugger Lab: Watch a Register Change
A cartridge written to be watched: breakpoints, single steps, registers and memory, with known answers
Audience: first-year computer architecture and programming students
Playing with RISC-V: Assembly, C, and Retro Games on the PRG32 Platform
Notes: Teaching support for Chapter 4 of the textbook. Practical, step-by-step session: learners work at their machines; keep each step to its time box. Preparation: PRG32-QT installed; toolchain active. Source: labs/04-prg32qt/probe.S (65 lines). Build it once: labs/run.sh is not needed here.

## Slide 2: Learning objectives
1
Build and import a cartridge into PRG32-QT
2
See the entry trampoline the builder adds
3
Stop after a call and read its result in a0
4
Follow a branch decision
5
Find a variable's address and watch its bytes change
6
Control the debugger from the command line
Notes: State the objectives; return to this slide at the end.

## Slide 3: Plan of the session
7'
8'
10'
11'
9'
1
Build and import
2
The trampoline
3
Input in a0
4
Memory
5
Scripted control
Notes: Total: 45 minutes.

## Slide 4: The cartridge we will watch
1
probe.S: 65 lines, three variables
2
frames: +1 every frame
3
buttons: the last input mask
4
box_x: moves by 2 with LEFT and RIGHT
5
Because we know the source, every reading has a known answer

## Slide 5: probe_update
probe_update:
addi sp, sp, -16
sw ra, 12(sp)
call prg32_input_read # a0 = button mask <-- breakpoint
target
la t0, buttons
sw a0, 0(t0) # remember it so the debugger can find
it
la t0, frames
lw t1, 0(t0)
addi t1, t1, 1 # one tick per frame
sw t1, 0(t0)
la t0, box_x
lw t2, 0(t0)
andi t3, a0, 1 # LEFT?
beqz t3, 1f
addi t2, t2, -2
1: andi t3, a0, 2 # RIGHT?
beqz t3, 2f
addi t2, t2, 2
2: sw t2, 0(t0)
Screenshot: this step, built and run
Read input, store it, count a frame, move box_x. The screenshot: RIGHT held for 40 frames moved the box from 152 to 232.
Notes: Source: labs/04-prg32qt/probe.S

## Slide 6
01
Build and import
Your own cartridge on a third host

## Slide 7: Build the probe
1
cd $PRG32_HOME
2
python3 -m prg32 cartridge build ../Playing-with-RISC-V_PRG32_textbook/labs/04-prg32qt/probe.S --portable --entry-prefix probe --name probe --out work/probe.prg32
3
Note code= from the log
Step 1
about 3 min
Expected result
[OK] built ... code=2780 mem=2780.

## Slide 8: Import and enable debug mode
1
In PRG32-QT import work/probe.prg32 and run it
2
Move the box with the arrow keys; press Escape
3
Settings: enable 'Run cartridges in RISC-V debug mode'
4
Run it again
Step 2 | about 4 min
Expected result
A yellow box and a green bar growing along the top; then the same with the debugger panel beside it.
Notes: Screenshot: this step, built and run: labs/04-prg32qt/expected/probe.png

## Slide 9
02
The trampoline
What the console really calls

## Slide 10: Select Update: this is not your code yet
prg32_entry_update:
addi sp, sp, -16
sw ra, 12(sp)
la t0, __prg32_abi
sw a0, 0(t0) # the host passes the ABI table in a0
call probe_update # now your function
lw ra, 12(sp)
addi sp, sp, 16
ret
1
Generated by the cartridge builder
2
It saves the table pointer for the stubs
3
Then it calls your update
Notes: From prg32/cartridge/build_cartridge.py. The disassembly shows auipc/addi pairs for la and call.

## Slide 11: Step into your function
1
Select the Update view and press Pause
2
Step until the highlighted row enters probe_update
3
Note pc, sp and ra
4
Step once more (the addi sp): note sp again
Step 3
about 6 min
Expected result
In the trampoline sp goes 0x40842000 -> 0x40841ff0; in probe_update it goes to 0x40841fe0. ra = 0x40800aa8, an address inside the trampoline: where probe_update must return.

## Slide 12: A real trace of one update
pc instruction what changed
0x40800a90 c.addi sp, -16 sp = 0x40841ff0
0x40800a94 la t0, __prg32_abi t0 = 0x40800ad8
0x40800a9c sw a0, 0(t0) saves 0x40840000
0x40800aa0 call probe_update ra = 0x40800aa8
0x40800002 c.addi sp, -16 sp = 0x40841fe0
0x40800006 call (the stub) ra = 0x4080000e
0x408000be la t0 / lw t0 t0 = 0x40840000
0x408000ca lw t1, 24(t0) t1 = 0xf0000004
0x408000ce c.jr t1 a0 = 0x0
0x4080000e la t0, buttons t0 = 0x40800ad0
1
Rows 1-4: the trampoline saves the table pointer and calls you
2
Rows 5-6: your prologue and your call
3
Rows 7-9: the stub reads table entry 1 (offset 24) and jumps to the host
4
a0 = 0: no key held
Notes: Recorded from PRG32-QT 0.4.1 through its /api/debug interface, single-stepping labs/04-prg32qt/probe.S.

## Slide 13: Check your understanding
pc advanced by 2, not 4, after one step. Why?
A
A step was skipped
B
The instruction has a 16-bit compressed encoding
C
pc counts in half-words
D
It was a branch
Notes: Answer: B. RV32IMAC: the C extension encodes common instructions in 16 bits.

## Slide 14
03
Input in a0
A return value, seen in a register

## Slide 15: Break after the input call
1
In probe_update find the call to prg32_input_read
2
Click the gutter beside the NEXT instruction (the la t0, buttons)
3
Make sure the bug toggle is highlighted; press Resume
4
It stops there once per frame
Step 4
about 5 min
Expected result
Execution stops at 0x4080000e, immediately after the input read, once per frame: 'frames' is one higher at each stop.

## Slide 16: Read the mask
1
No key held: Resume, read a0
2
Hold LEFT, Resume, read a0
3
Hold LEFT and Z, Resume, read a0
4
Hold RIGHT, Resume, read a0
Step 5
about 5 min
Expected result
0x00000000, 0x00000001, 0x00000011, 0x00000002.
Notes: Input is frozen while paused: hold the key, then press Resume. The no-key reading was recorded from the real application; the key-held values follow from the button masks.

## Slide 17: Explain the readings
Keys held | a0 | Bits set
none | 0x00 | -
LEFT | 0x01 | bit 0
LEFT + A | 0x11 | bits 0 and 4
RIGHT | 0x02 | bit 1

## Slide 18: Follow the decision
1
With RIGHT held, step from the breakpoint to 'andi t3, a0, 1'
2
Step it: read t3
3
Step the beqz: did pc jump?
4
Step on to 'andi t3, a0, 2' and its beqz
Step 6
about 5 min
Expected result
t3 = 0 after the LEFT test, so the first beqz jumps over the addi. After the RIGHT test t3 = 2 and the second beqz falls through.

## Slide 19
04
Memory
Find a variable and watch it

## Slide 20: Get an address from a register
1
Step until just after 'la t0, box_x' in probe_update
2
Read t0: this is the ADDRESS of box_x
3
Type it in the memory field and press Inspect
4
Read the first four bytes
Step 7
about 6 min
Expected result
t0 = 0x40800ad4. The four bytes there are 98 00 00 00: 0x98 = 152, little-endian.

## Slide 21: Reading a little-endian word
1
Memory shows bytes in address order
2
RISC-V stores the least significant byte first
3
98 00 00 00 is 0x00000098 = 152
4
e8 00 00 00 is 0x000000e8 = 232
5
04 01 00 00 would be 0x00000104 = 260
98 00 00 00
= 152

## Slide 22: Watch it change
1
Remove the breakpoint; Resume
2
Hold RIGHT for about a second; Pause
3
Inspect the same address again
4
Inspect 0x40800acc: frames, buttons, box_x are three consecutive words
Step 8
about 5 min
Expected result
At 0x40800acc: frames (it grows by one per frame: 3b, 3c, 3d...), then buttons (0 when nothing is held), then box_x, which grew by 2 per frame held.

## Slide 23: Check your understanding
box_x shows 'e8 00 00 00'. For how many frames was RIGHT held since 152?
A
232
B
80
C
40
D
20
Notes: Answer: C. (232 - 152) / 2 = 40.

## Slide 24
05
Scripted control
The debugger as an instrument

## Slide 25: Find the device and pause it
1
Read the device URL shown by PRG32-QT
2
python3 -m prg32 runtime --url http://HOST:PORT
3
python3 -m prg32 debug enable --url http://HOST:PORT
4
python3 -m prg32 debug pause --url http://HOST:PORT
Step 9
about 4 min
Expected result
JSON with "firmware_version": "qt-0.4.1", "cart_abi_minor": 6 and the loaded cartridge; then the game freezes.

## Slide 26: Step and read from a script
1
python3 -m prg32 debug step --url http://HOST:PORT
2
python3 -m prg32 debug state --url http://HOST:PORT
3
Find pc and a0 in the reply
4
python3 -m prg32 debug resume --url http://HOST:PORT
Step 10
about 5 min
Expected result
Each step retires one instruction; state returns pc, paused, phase (update or draw), speed, breakpoints, the 32 registers and a memory dump as JSON.

## Slide 27: Discussion
1
Which claim from the lecture did you verify with your own eyes?
2
Why is the first code in Update not yours?
3
What can this debugger not tell you about the real board?
4
How would you automate a check that a function preserves s0?

## Slide 28: You can now
1
Build and debug a cartridge in PRG32-QT
2
Explain the entry trampoline
3
Read a return value in a0 and follow a branch
4
Take an address from a register and inspect memory
5
Decode a little-endian word
6
Drive the debugger from the command line

## Slide 29: Next steps and reading
Before the next session
Assembly track: use this debugger in every lab
Write up the a0 table and the box_x reading
Read PRG32-QT docs/DEBUGGING.md
Reading and sources
Textbook, Chapter 4
labs/04-prg32qt/probe.S
PRG32-QT docs/DEBUGGING.md
PRG32 docs/software/api.md (debugger API)