## Slide 1
CHAPTER 6 | LECTURE | 45 MINUTES
State and Input: Branches, Bitmasks, and Boundaries
How a processor decides, how it reads a controller, and how to keep an object on the screen
Audience: computer architecture students (RISC-V assembly track)
Playing with RISC-V: Assembly, C, and Retro Games on the PRG32 Platform
Notes: Teaching support for Chapter 6 of the textbook. Front lecture: about 45 minutes including the questions.

## Slide 2: Learning objectives
1
Read and write conditional branches and local labels
2
Translate if and if-else into branch patterns
3
Isolate one button from the input bitmask with andi
4
Move an object under joystick control
5
Implement a two-sided boundary clamp
6
Apply a systematic debugging method
Notes: State the objectives; return to this slide at the end.

## Slide 3: Agenda
10'
9'
9'
9'
8'
1
Decisions: the branch
2
Reading the controller
3
Moving an object
4
The boundary clamp
5
Debugging like a systems programmer
Notes: Total: 45 minutes.

## Slide 4
A branch is the only way a processor ever makes a decision.
if, else, while, for, switch: all of them become compare-and-branch.

## Slide 5: Conditional branches
Instruction | Branch to the label if
beq rs1, rs2, L | rs1 == rs2
bne rs1, rs2, L | rs1 != rs2
blt rs1, rs2, L | rs1 < rs2 (signed)
bge rs1, rs2, L | rs1 >= rs2 (signed)
bltu, bgeu | the same comparisons, unsigned
Notes: Otherwise execution falls through to the next instruction.

## Slide 6: beq rs1, rs2, label as 32 bits
31..25
imm[12|10:5]
offset high
7 bit
24..20
rs2
5 bit
19..15
rs1
5 bit
14..12
funct3
000 = beq
3 bit
11..7
imm[4:1|11]
offset low
5 bit
6..0
opcode
1100011
7 bit
B-type. The immediate is a signed offset from the branch itself, in multiples of 2 bytes: a branch reaches about 4 KiB either way. Farther targets need a jump.

## Slide 7: Branches are relative, so code can move
1
A branch stores a distance, not an address
2
The same bytes work wherever the cartridge is loaded
3
la uses auipc: also relative to the pc
4
This is what lets one cartridge run at different addresses on different hosts

## Slide 8: Pseudo-branches against zero
You write | Means
beqz rs, L | branch if rs == 0
bnez rs, L | branch if rs != 0
bltz rs, L | branch if rs < 0
bgez rs, L | branch if rs >= 0
blez, bgtz | <= 0, > 0
ble, bgt | swap the operands of bge, blt
j L | always jump

## Slide 9: An 'if' is a branch around code
C
if (x < 0) {
x = 0;
}
next();
Assembly
bgez t2, 1f # skip if x >= 0
li t2, 0
1:
call next
Notes: The branch tests the opposite condition: it jumps over the body when the if is false.

## Slide 10: Local labels: 1f and 1b
1
A digit followed by a colon is a local label
2
1f means the next label 1, forward
3
1b means the previous label 1, backward
4
They can be reused, so short skips need no invented names

## Slide 11: The if-else pattern
1
Test
Branch to 'else' when the condition is false.
2
Then-part
The code for true; end it with 'j end'.
3
Else-part
The label 'else' and its code.
4
End
The label 'end': both paths meet.
Notes: Forgetting the 'j end' makes the then-part fall through into the else-part.

## Slide 12: Check your understanding
Which instruction skips the next line when t0 is not zero?
A
beqz t0, 1f
B
bnez t0, 1f
C
bgez t0, 1b
D
j 1f
Notes: Answer: B. bnez branches when the register is non-zero.

## Slide 13
01
Reading the controller
One call, one integer, seven bits

## Slide 14: Read once, keep a copy
call prg32_input_read # button bitmask returned in a0
mv t0, a0 # keep our own copy in t0 before anything else
1
The bitmask returns in a0
2
a0 is destroyed by the next call: copy it
3
Read input once per frame, at the top of update
Notes: Source: examples/asm_state_and_input/get_input.S

## Slide 15: One bit per button
Button | Mask | Bit
LEFT | 1 | 0
RIGHT | 2 | 1
UP | 4 | 2
DOWN | 8 | 3
A | 16 | 4
B | 32 | 5
START / SELECT | 64 | 6

## Slide 16: Test one button
andi t3, t0, 1 # PRG32_BTN_LEFT is bit 0 (value 1)
beqz t3, 1f # if the LEFT bit is clear, skip the add
addi t1, t1, -1 # LEFT is pressed: move the object left
1: ...
1
andi keeps only bit 0
2
t3 is 0 or 1: nothing else
3
beqz skips the action when the bit is clear
Notes: Source: examples/asm_state_and_input/button_test.S

## Slide 17: Any bit, with a shift: the lamp loop of Lab 2
la t0, buttons
lw t1, 0(t0)
srl t1, t1, s0 # move bit number s0 down to bit 0
andi t1, t1, 1
li a4, GREY
beqz t1, 1f
li a4, YELLOW
1
srl moves bit number s0 down to bit 0
2
andi keeps only that bit
3
The colour depends on the result
Notes: Source: labs/06-asm-state-and-input/step1_lamps.S

## Slide 18: Why andi and not beq
1
Several buttons can be held at once
2
andi isolates the bit you care about, ignoring the rest
3
beq against the mask is true only if no other button is held
4
This is how every memory-mapped status register is read

## Slide 19: Check your understanding
a0 = 0x12. Which tests succeed?
A
LEFT only
B
RIGHT and A
C
UP and B
D
RIGHT only
Notes: Answer: B. 0x12 = 0001 0010: bit 1 (RIGHT) and bit 4 (A).

## Slide 20
02
Moving an object
Input changes state; draw shows it

## Slide 21: The shape of update
Read input
a0, copy to t0
Load x
la, lw
Test LEFT
andi, beqz, addi -1
Test RIGHT
andi, beqz, addi +1
Clamp and store
sw
Load the variable once, adjust it in a register through all the tests, store it once at the end.

## Slide 22: LEFT and RIGHT move x
call prg32_input_read # the result is stored in a0
mv t0, a0 # t0 now stores the input result
la t1, game_x # t1 = game_x address
lw t2, 0(t1) # t2 = game_x value
andi t3, t0, 1 # test LEFT (bit 0)
beqz t3, 1f
addi t2, t2, -1 # move left
# when an update occurs, we want to take note
# that the screen should update
li t4, 1
la t5, text_update
sw t4, 0(t5)
1: andi t3, t0, 2 # test RIGHT (bit 1)
beqz t3, 2f
addi t2, t2, 1 # move right
li t4, 1
la t5, text_update
sw t4, 0(t5)
2: sw t2, 0(t1) # store the new x
1
t0 = buttons, t2 = x
2
Each test may adjust t2
3
One store at label 2
Notes: The full file is examples/asm_state_and_input/input_read.S. Source: examples/asm_state_and_input/input_read.S

## Slide 23: Speed is a number per frame
1
Adding 1 per frame at 30 frames per second moves 30 units per second
2
On a 40-column console that crosses the screen in just over a second
3
On a 320-pixel screen use 3 or 4 pixels per frame
4
Speed, frame rate, and screen size are one design decision

## Slide 24
03
The boundary clamp
Staying on the screen

## Slide 25: A two-sided clamp
bltz t2, 3f # if x < 0, clamp to the left edge
li t3, 39 # maximum column
ble t2, t3, 4f # if x <= 39, it is already in range
mv t2, t3 # otherwise clamp to the right edge
j 4f
3: li t2, 0 # left clamp
4: sw t2, 0(t1) # store the bounded x
1
Below zero: go to label 3
2
Not above 39: already fine, go to 4
3
Above: replace with the maximum
4
Label 4 stores the bounded value
Notes: Source: examples/asm_state_and_input/x_clamping.S

## Slide 26: Choosing the limits
1
Minimum is 0
2
Maximum is screen size minus object size
3
Text console, one character: 39
4
320-pixel viewport, 64-pixel paddle: 256
5
Clamp after moving, before storing
320 - 64
= 256, the paddle's last legal x

## Slide 27: Check your understanding
A 16-pixel sprite on a 320-pixel screen: the largest legal x?
A
320
B
319
C
304
D
336
Notes: Answer: C. 320 - 16 = 304.

## Slide 28: Clamp or wrap
Clamp
Stop at the edge
Paddles, walls, players
Two compares, two assignments
Wrap
Reappear on the other side
Asteroids, endless runners
Add or subtract the screen size

## Slide 29
04
Debugging
A method, not a mood

## Slide 30: Debugging like a systems programmer
1
Reproduce
Make the failure happen on demand, with the fewest inputs.
2
Predict
Write down what each register should hold.
3
Observe
Print with hex32, or stop in the debugger.
4
Bisect
Halve the suspect region until one instruction is left.

## Slide 31: Symptoms and usual causes
Symptom | Usual cause
Object never moves | Missing sw, or testing the wrong bit
Moves the wrong way | Sign of the addi
Leaves the screen | Clamp missing, or applied before the move
Works once, then hangs | ra not saved, or stack not restored
Value changes on its own | A t register assumed to survive a call

## Slide 32: Checkpoint
1
Write an if as a branch around code
2
Test any button with andi and beqz
3
Explain why input is copied out of a0
4
Write a clamp for a given object width
5
Describe the four debugging steps

## Slide 33: Next steps and reading
Before the next session
Lab: joystick-driven marker with a clamp
Read Chapter 7: graphics and collision
Memorise the button masks
Reading and sources
Textbook, Chapter 6
PRG32 docs/learn/labs/lab_02_input.md
PRG32 docs/learn/labs/debugging_memory_inspection.md
RISC-V Assembly Programmer's Manual