## Slide 1
CHAPTER 7 | LECTURE | 45 MINUTES
Drawing the Game: Graphics, Collision, and the Frame
From a blank frame to a complete Pong in RISC-V assembly
Audience: computer architecture students (RISC-V assembly track)
Playing with RISC-V: Assembly, C, and Retro Games on the PRG32 Platform
Notes: Teaching support for Chapter 7 of the textbook. Front lecture: about 45 minutes including the questions.

## Slide 2: Learning objectives
1
Call a framework function with up to eight register arguments
2
Draw a frame: clear, then rectangles from state
3
Model motion as position plus velocity, with bounces
4
Detect a rectangle collision with one call and act on the result
5
Assemble update and draw into a complete game
6
Explain the incremental order in which the game was built
Notes: State the objectives; return to this slide at the end.

## Slide 3: Agenda
5'
9'
10'
9'
7'
5'
1
A blank frame
2
Drawing rectangles
3
The ball: velocity and bounce
4
Collision
5
The complete game
6
How it was built
Notes: Total: 45 minutes.

## Slide 4
Every picture a game shows is rebuilt from numbers, thirty times a second.
Draw never remembers the last frame. State does.

## Slide 5: A blank frame
blank_draw:
addi sp, sp, -16
sw ra, 12(sp)
li a0, 0 # RGB565 black
call prg32_gfx_clear # fill the 320x200 viewport
lw ra, 12(sp)
addi sp, sp, 16
1
draw calls a helper, so it needs a frame
2
One argument: the colour, in a0
3
0 is black in RGB565
Notes: Source: examples/asm_graphics_game/hello_world_graphics.S

## Slide 6: Why clear every frame
1
The framebuffer keeps whatever was drawn last
2
Without a clear, a moving object leaves a trail
3
Clear, then draw every object from current state
4
Order matters: later rectangles cover earlier ones

## Slide 7
01
Drawing rectangles
Five arguments, five registers

## Slide 8: What a drawing call costs
1
prg32_gfx_clear writes all 64,000 bytes of the framebuffer
2
A 64 x 8 paddle writes 512
3
An 8 x 8 ball writes 64
4
Clearing dominates: a whole Pong frame is about 64,600 bytes written
5
On the board the frame is then sent to the display 8 rows at a time over SPI
64,000
bytes per clear

## Slide 9: prg32_gfx_rect(x, y, w, h, color)
Argument | Register | Paddle example
x | a0 | value of paddle_x, loaded from memory
y | a1 | 188
w | a2 | 64
h | a3 | 8
color | a4 | 65535 (white)

## Slide 10: Drawing the paddle from state
la t0, paddle_x # address of the paddle position
lw a0, 0(t0) # a0 = x (a value read from memory)
li a1, 188 # a1 = y (near the bottom)
li a2, 64 # a2 = width
li a3, 8 # a3 = height
li a4, 65535 # a4 = white (RGB565 0xffff)
call prg32_gfx_rect # draw the paddle
1
x comes from memory: it is state
2
y, w, h, colour are constants
3
Arguments are set immediately before the call
Notes: Source: examples/asm_graphics_game/paddle_draw.S

## Slide 11: What those numbers mean on screen
paddle
(0,0)
x=128 y=188
320 x 200 game viewport
1
y = 188 puts an 8-high paddle 4 pixels above the bottom
2
x ranges from 0 to 256
3
The rectangle's corner is its top-left

## Slide 12: Decimal colours in listings
1
65535 = 0xFFFF = white
2
65504 = 0xFFE0 = yellow
3
0 = black
4
Use .equ to give them names in your own code
0xFFFF
65535, white

## Slide 13: Check your understanding
Which register carries the height of the rectangle?
A
a1
B
a2
C
a3
D
a4
Notes: Answer: C. x a0, y a1, w a2, h a3, colour a4.

## Slide 14
02
The ball
Position, velocity, and the bounce

## Slide 15: Motion is two numbers per axis
1
Position
ball_x, ball_y: where the ball is now, in pixels.
2
Velocity
ball_dx, ball_dy: how far it moves each frame, with a sign.
3
Update rule
x = x + dx; y = y + dy. Once per frame.
4
Bounce
At an edge, negate the velocity on that axis and clamp the position.

## Slide 16: Horizontal motion and two bounces
# --- BALL X MOVEMENT ---
la t1, ball_x
lw t2, 0(t1) # t2 = ball x
la t3, ball_dx
lw t4, 0(t3) # t4 = ball dx
add t2, t2, t4 # x = x + dx
# Check Left Edge (x < 0)
bgez t2, check_right_edge
li t2, 0 # clamp to left edge
neg t4, t4 # reverse direction
j save_ball_x
check_right_edge:
li t5, 312 # 320 - ball width (8)
ble t2, t5, save_ball_x
mv t2, t5 # clamp to right edge
neg t4, t4 # reverse direction
save_ball_x:
sw t2, 0(t1) # store new x
1
Load position and velocity
2
Add: the motion itself
3
Left edge: clamp to 0, negate dx
4
Right edge: 312 = 320 - 8
5
Store both back
Notes: Source: examples/asm_graphics_game/ball_motion.S

## Slide 17: Why clamp as well as negate
1
The ball can step past the edge by up to |dx| pixels
2
Negating alone leaves it outside for a frame
3
It may then be negated again: it sticks to the wall
4
Clamp puts it exactly on the edge; negate sends it back

## Slide 18: Vertical motion: only the top bounces
# --- BALL Y MOVEMENT ---
la t1, ball_y
lw t2, 0(t1) # t2 = ball y
la t3, ball_dy
lw t4, 0(t3) # t4 = ball dy
add t2, t2, t4 # y = y + dy
# Check Top Edge (y < 0)
bgez t2, save_ball_y
li t2, 0 # clamp to top edge
neg t4, t4 # reverse direction (bounce down)
save_ball_y:
sw t2, 0(t1) # store new y
1
Same pattern on the y axis
2
Only y < 0 is handled here
3
The bottom is the paddle's job, or a lost ball
Notes: Source: examples/asm_graphics_game/ball_motion.S

## Slide 19: Check your understanding
The ball is 8 wide. Why is the right limit 312?
A
The screen is 312 wide
B
320 minus the ball width keeps its right edge on screen
C
It leaves room for the score
D
It is a typo
Notes: Answer: B. limit = screen size - object size.

## Slide 20
03
Collision
Did they touch?

## Slide 21: What the overlap test computes
/* two axis-aligned rectangles overlap when they overlap on x AND on
y */
int hit = ax < bx + bw && /* a's left is left of b's right */
ax + aw > bx && /* a's right is right of b's left */
ay < by + bh && /* a's top is above b's bottom */
ay + ah > by; /* a's bottom is below b's top */
1
Four comparisons
2
Touching edges do not count
3
Works with negative coordinates
Notes: This is the test the Construction Kit simulator uses for the same call.

## Slide 22: Rectangle overlap
Ball rectangle
x, y, 8, 8
Paddle rectangle
x, 188, 64, 8
prg32_sprite_hitbox
8 arguments
a0
non-zero if they overlap
Two axis-aligned rectangles overlap when they overlap on x and on y. The framework tests it; you supply eight numbers and read one.

## Slide 23: Eight arguments, a0 to a7
la t0, ball_x
lw a0, 0(t0) # a0 = ball x
la t0, ball_y
lw a1, 0(t0) # a1 = ball y
li a2, 8 # a2 = ball width
li a3, 8 # a3 = ball height
la t0, paddle_x
lw a4, 0(t0) # a4 = paddle x
li a5, 188 # a5 = paddle y
li a6, 64 # a6 = paddle width
li a7, 8 # a7 = paddle height
call prg32_sprite_hitbox # a0 = non-zero if overlapping
1
Ball: a0..a3
2
Paddle: a4..a7
3
The result replaces a0
4
beqz skips the reaction
Notes: Source: examples/asm_graphics_game/collision_detection.S

## Slide 24: Reacting to the hit
# reverse direction
la t0, ball_dy
lw t1, 0(t0)
blez t1, no_overlap # only bounce if ball is moving down (t1 >
0)
neg t1, t1 # Reverse dy natively
sw t1, 0(t0)
1
Load dy
2
blez: bounce only if the ball is moving down
3
Negate and store
Notes: The guard is the important line: without it an overlapping ball flips direction every frame. Source: examples/asm_graphics_game/collision_detection.S

## Slide 25: One hit, one bounce
1
The ball may overlap the paddle for several frames
2
Negating on every overlapping frame makes it jitter in place
3
Guard on direction: bounce only while dy is positive
4
The same guard prevents counting one hit many times

## Slide 26: Check your understanding
No guard: a ball moving down overlaps the paddle for exactly 2 frames. Afterwards it moves?
A
Up
B
Down: negated twice, it passes through
C
It stops
D
Sideways
Notes: Answer: B. Two negations restore the original direction. The guard makes the bounce happen once.

## Slide 27
04
The complete game
update and draw, assembled

## Slide 28: The order inside update
1
Input
Read buttons; move and clamp the paddle.
2
Ball x
Add dx; bounce off left and right.
3
Ball y
Add dy; bounce off the top.
4
Collision
Hitbox against the paddle; bounce upward.
Notes: State changes only here. Nothing is drawn.

## Slide 29: The complete draw
pong_skeleton_draw:
addi sp, sp, -16
sw ra, 12(sp)
li a0, 0 # RGB565 black
call prg32_gfx_clear # black background
la t0, paddle_x # draw the paddle
lw a0, 0(t0)
li a1, 188
li a2, 64
li a3, 8
li a4, 65535 # RGB565 white
call prg32_gfx_rect
la t0, ball_x # draw the ball
lw a0, 0(t0)
la t0, ball_y
lw a1, 0(t0)
li a2, 8
li a3, 8
li a4, 65504 # yellow
call prg32_gfx_rect
lw ra, 12(sp)
1
Frame
2
Clear to black
3
Paddle from paddle_x
4
Ball from ball_x, ball_y
5
Epilogue follows
Notes: Source: examples/asm_graphics_game/pong_skeleton.S

## Slide 30: What the state section contains
1
paddle_x: one word
2
ball_x, ball_y: two words
3
ball_dx, ball_dy: two signed words
4
Five words, twenty bytes: the entire game state
20 bytes
of state for a complete Pong

## Slide 31
05
How it was built
The method matters more than the listing

## Slide 32: Step by step
1
Blank frame
Three returns; then a clear.
2
Paddle
Draw it from a variable; then move it; then clamp it.
3
Ball
Draw it; add x motion; add y motion.
4
Collision
Hitbox; guard; sound last.
Notes: Each step was built, run, and verified by eye before the next began.

## Slide 33: Checkpoint
1
Place five arguments for prg32_gfx_rect
2
Explain clamp-and-negate
3
List the eight hitbox arguments in order
4
Say why the bounce is guarded by direction
5
State the order of work inside update

## Slide 34: Next steps and reading
Before the next session
Lab: build Pong in four verified steps
Read Chapter 8: the capstone
Bring your paper design from Chapter 2
Reading and sources
Textbook, Chapter 7
examples/asm_graphics_game/ in the textbook repository
PRG32 docs/learn/tutorial_graphic_game.md
PRG32 docs/learn/labs/lab_03_graphics.md