## Slide 1
CHAPTER 16 | LECTURE | 45 MINUTES
Assembly Meets C: One Game, Two Altitudes
The same logic in two languages, what a compiler does, and what C hides and does not hide
Audience: computer architecture and programming students (both tracks)
Playing with RISC-V: Assembly, C, and Retro Games on the PRG32 Platform
Notes: Teaching support for Chapter 16 of the textbook. Front lecture: about 45 minutes including the questions.

## Slide 2: Learning objectives
1
Map a C statement onto the instructions that implement it
2
Explain what a compiler decides for you
3
List what C hides and what it leaves visible
4
Relate the calling convention to C function calls
5
Choose a language for a task with reasons
6
Read compiler output as a learning tool
Notes: State the objectives; return to this slide at the end.

## Slide 3: Agenda
10'
9'
9'
9'
8'
1
The same logic, twice
2
What the compiler decides
3
What C hides and does not
4
A side-by-side map
5
Where to go next
Notes: Total: 45 minutes.

## Slide 4
The addi you traced on Monday is the machine that ran your C on Thursday.
This session shows the join.

## Slide 5: Move the paddle left: C
uint32_t input = prg32_input_read();
if (input & PRG32_BTN_LEFT) {
paddle_x -= 3;
}
1
One declaration
2
One condition
3
One assignment
4
The intent is on the page
Notes: Source: examples/assembly_meets_c/move_left_c.c

## Slide 6: Move the paddle left: assembly
call prg32_input_read # input bitmask in a0
mv t0, a0 # keep our copy
la t1, paddle_x
lw t2, 0(t1) # load paddle_x from memory
andi t3, t0, 1 # isolate the LEFT bit
beqz t3, 1f # if LEFT is clear, skip
addi t2, t2, -3 # paddle_x -= 3
1: sw t2, 0(t1) # store paddle_x back
1
The call and its result in a0
2
The address, then the value
3
The mask and the branch
4
The store back to memory
Notes: Source: examples/assembly_meets_c/move_left_asm.S

## Slide 7: Line by line
C | Assembly | What happened
input = prg32_input_read(); | call ...; mv t0, a0 | Result arrives in a0; a register is chosen for 'input'
input & PRG32_BTN_LEFT | andi t3, t0, 1 | The constant's value, 1, is used directly
if ( ... ) { } | beqz t3, 1f | Branch around the body when false
paddle_x -= 3; | lw; addi -3; sw | Load, modify, store

## Slide 8: One statement, three instructions
1
paddle_x lives in memory; arithmetic happens in registers
2
So every change is load, compute, store
3
C writes it as one operator: -=
4
The cost did not disappear; the notation did

## Slide 9: Check your understanding
How many memory accesses does 'paddle_x -= 3;' need, at least?
A
None
B
One
C
Two: a load and a store
D
Three
Notes: Answer: C. A load and a store, unless the compiler keeps the variable in a register across statements.

## Slide 10
01
What the compiler decides
Decisions you made by hand in the assembly track

## Slide 11: Four decisions
1
Register allocation
Which variable lives in which register, and when.
2
Stack frames
How much to reserve; which registers to save; when ra must be saved.
3
Instruction selection
addi or add; a shift instead of a multiply; a compressed encoding.
4
Layout
Where each function and variable is placed in the cartridge.

## Slide 12: You, then the compiler
By hand
You chose t2 for x
You wrote the prologue
You remembered that t registers die at a call
You picked labels
Compiled
It chooses, and may change its mind per line
It emits the prologue only when needed
It knows the convention exactly
It invents labels

## Slide 13: Optimisation changes the picture
1
Without optimisation, every statement loads and stores: easy to follow
2
With it, variables stay in registers and code is reordered
3
Both are correct translations of the same C
4
Read unoptimised output to learn; optimised output to be impressed

## Slide 14: Seeing it yourself
riscv32-esp-elf-gcc -S -O0 -march=rv32imac -mabi=ilp32 \
-Icomponents/prg32/include -Icomponents/prg32_audio/include \
work/pong/pong.c -o pong_O0.s
riscv32-esp-elf-gcc -S -Os -march=rv32imac -mabi=ilp32 \
-Icomponents/prg32/include -Icomponents/prg32_audio/include \
work/pong/pong.c -o pong_Os.s
1
-S stops after generating assembly
2
-O0: no optimisation
3
-Os: optimise for size
4
Compare the two files

## Slide 15: gcc -O0: every statement stands alone
pong_c_update:
addi sp,sp,-32
sw ra,28(sp)
sw s0,24(sp)
addi s0,sp,32
call prg32_input_read
sw a0,-20(s0)
lw a5,-20(s0)
andi a5,a5,1
beq a5,zero,.L3
lui a5,%hi(paddle_x)
lw a5,%lo(paddle_x)(a5)
addi a4,a5,-3
lui a5,%hi(paddle_x)
sw a4,%lo(paddle_x)(a5)
1
Frame pointer in s0
2
input stored, then reloaded
3
paddle_x: its address is rebuilt for the load and again for the store
Notes: Real output for the C Lab 1 Pong. Source: labs/16-assembly-meets-c/pong_c_update_O0.s

## Slide 16: gcc -Os: the same C, rearranged
pong_c_update:
addi sp,sp,-32
sw s0,24(sp)
sw ra,28(sp)
sw s1,20(sp)
sw s2,16(sp)
sw s3,12(sp)
call prg32_input_read
andi a5,a0,1
lui s0,%hi(paddle_x)
beq a5,zero,.L3
lw a5,%lo(paddle_x)(s0)
addi a5,a5,-3
sw a5,%lo(paddle_x)(s0)
1
No frame pointer
2
input never leaves a0
3
The address of paddle_x is kept in s0
4
Three instructions per update
Notes: Real output for the same file. Source: labs/16-assembly-meets-c/pong_c_update_Os.s

## Slide 17: The same function, counted
 | gcc -O0 | gcc -Os | by hand
Lines for update | 114 | 83 | 74
Whole file | 223 | 192 | 139
Cartridge | - | 2952 bytes | 3052 bytes
Notes: The hand-written figures are the assembly Pong with the same features (Lab 4, step 7).

## Slide 18: Check your understanding
Who decides that a function must save ra?
A
The linker
B
The C programmer, with a keyword
C
The compiler, because the function calls another
D
The runtime
Notes: Answer: C. A non-leaf function gets a frame that saves ra.

## Slide 19
02
What C hides, and what it does not
An honest account of abstraction

## Slide 20: Hidden and not hidden
C hides
Registers and their roles
The stack frame
Branch targets and labels
Instruction encodings
C does not hide
The size and signedness of integers
Memory: arrays have no bounds checks
Addresses: & and pointers are real
Bits: masks and shifts are everyday tools
Time: nothing is free

## Slide 21: Where C lets the machine show through
1
int overflows silently; uint8_t wraps at 255
2
bricks[10] in a ten-element array writes somewhere
3
A struct's fields are bytes at offsets: the platform actor is 24 bytes
4
The assembly track's actor offsets and the C struct describe the same memory

## Slide 22: One struct, two views
Field | C | Assembly offset
x | player.x | 0
y | player.y | 4
vx | player.vx | 8
vy | player.vy | 12
w, h | player.w, player.h | 16, 18
state | player.state | 20
Notes: prg32.h publishes both: the typedef for C and PRG32_PLATFORM_ACTOR_*_OFFSET constants for assembly.

## Slide 23
03
A side-by-side map
The whole course on one slide

## Slide 24: Concept by concept
Concept | Assembly | C
State | .data words and labels | file-scope static variables
Constant | .equ | #define or const
Decision | compare and branch | if / else
Repetition | backward branch | for / while
Function call | a0-a7, call, ra | f(x, y)
Grouped data | offsets from a base address | struct fields
Button test | andi + beqz | if (input & MASK)

## Slide 25: The boundary both languages share
1
'Call the framework' is the same boundary in assembly and in C
2
The cartridge ABI is defined at the level of registers, so both fit
3
A block from the Construction Kit crosses the same boundary through generated C
4
Three altitudes, one interface

## Slide 26: Three altitudes of one game
Blocks
if button LEFT pressed
C
if (input & PRG32_BTN_LEFT)
Assembly
andi t3, t0, 1 ; beqz
Machine code
32 or 16 bits per instruction
Each arrow is something a tool will show you: Generate C, gcc -S, and the PRG32-QT disassembly.

## Slide 27
04
Where to go next
Choosing and continuing

## Slide 28: Choosing a language
Reach for assembly when
You must know exactly what executes
A routine is tiny and critical
You are studying the machine
You are writing the first lines of a system
Reach for C when
The program has structure to manage
It must be read by others
It must be portable
Almost always, for whole programs

## Slide 29: Four ways to continue
1
Measure
Appendix B: frame timing on real hardware, like a scientist.
2
Publish
Chapter 17: the Cartridge Store.
3
Read
The richer examples: raycaster, Wing Commander, Blackjack.
4
Build
Appendix E: wire your own PRG32.

## Slide 30: Check your understanding
Which is NOT hidden by C?
A
Which register holds a variable
B
The stack frame layout
C
The fact that an array index is unchecked
D
Branch labels
Notes: Answer: C. C exposes memory honestly; bounds are your responsibility.

## Slide 31: Checkpoint
1
Translate a C if into compare-and-branch
2
Name four decisions a compiler makes
3
Give two things C does not hide
4
Relate struct fields to offsets
5
Argue for a language choice

## Slide 32: Next steps and reading
Before the next session
Lab: compile your own C to assembly and read it
Bring pong.c and your pong.S
Read Chapter 17
Reading and sources
Textbook, Chapter 16
examples/assembly_meets_c/ in the textbook repository
PRG32 docs/learn/teaching_with_prg32.md (comparing assembly and C)
Patterson and Hennessy, Computer Organization and Design, RISC-V edition