## Slide 1
CHAPTER 3 | LECTURE | 45 MINUTES
Setting Up Your Development Environment
Cross-compilation, ESP-IDF, the prg32 tool, two build directories, and how to diagnose a broken setup
Audience: first-year computer architecture and programming students
Playing with RISC-V: Assembly, C, and Retro Games on the PRG32 Platform
Notes: Teaching support for Chapter 3 of the textbook. Front lecture: about 45 minutes including the questions.

## Slide 2: Learning objectives
1
Explain what a cross-toolchain is and why we need one
2
Describe the role of ESP-IDF and why it must be activated in each shell
3
Name the two targets, their chips, and their build directories
4
Use the main prg32 commands for firmware and cartridges
5
Explain cartridge memory profiles
6
Diagnose the five most common setup failures
Notes: State the objectives; return to this slide at the end.

## Slide 3: Agenda
7'
8'
8'
10'
4'
8'
1
Host and target
2
ESP-IDF and activation
3
Two targets, two directories
4
The prg32 tool
5
Profiles
6
When it goes wrong
Notes: Total: 45 minutes.

## Slide 4
Your laptop is not the machine your program runs on.
Everything in this chapter follows from that one sentence.

## Slide 5: Host and target
Host: your laptop
x86-64 or ARM64 processor
Windows, Linux, or macOS
Runs the compiler and tools
Gigabytes of memory
Target: the PRG32 machine
32-bit RISC-V processor
No operating system you log in to
Runs the firmware and your cartridge
512 KB of RAM

## Slide 6: Cross-compilation
Source
.S or .c on the host
riscv32-esp-elf-gcc
runs on the host
RISC-V machine code
cannot run on the host
Target
board, QEMU, PRG32-QT
A cross-compiler runs on one architecture and produces code for another. Its name says so: riscv32-esp-elf-gcc.

## Slide 7: Check your understanding
Why can you not simply run the compiled cartridge on your laptop?
A
It has no file extension
B
It contains RISC-V instructions your laptop's CPU does not execute
C
It is encrypted
D
It needs administrator rights
Notes: Answer: B. Different instruction set. You need a RISC-V processor, an emulator of one, or an interpreter.

## Slide 8
01
ESP-IDF
Espressif's development framework for these microcontrollers

## Slide 9: What ESP-IDF provides
1
Compiler
The RISC-V GCC cross-toolchain for the ESP32-C3 and ESP32-C6.
2
Build system
idf.py, CMake, and Ninja: build, flash, monitor.
3
Drivers and RTOS
Wi-Fi, SPI, I2S, flash, and FreeRTOS, used by the PRG32 firmware.
4
QEMU
Espressif's emulator, installed as an optional tool.
Notes: Use ESP-IDF 5.4 or newer, installed for esp32c3 and esp32c6.

## Slide 10: Activation: the one idea behind every setup
1
Installing ESP-IDF does not change your shell
2
Each new terminal must 'source' export.sh to put the tools on the PATH
3
On Windows, open the ESP-IDF PowerShell shortcut instead
4
Almost every setup problem is ESP-IDF not being active in the current shell
export.sh
in every new terminal

## Slide 11: A quality-of-life alias
# in ~/.bashrc or ~/.zshrc
alias get_idf=". $HOME/esp-idf/export.sh"
alias prg="python3 -m prg32"
# then, in any new terminal:
get_idf
cd ~/PRG32
prg doctor
1
One word activates the toolchain
2
doctor checks compiler, idf.py, and the partition table

## Slide 12: Installation at a glance
System | Prerequisites | ESP-IDF
Windows | Git, Python 3 | ESP-IDF Tools Installer; use the ESP-IDF PowerShell
Linux (Debian/Ubuntu) | apt packages: cmake, ninja, libusb, portaudio... | git clone v5.4, install.sh esp32c3,esp32c6
macOS | Homebrew: cmake, ninja, dfu-util, portaudio... | git clone v5.4, install.sh esp32c3,esp32c6
Notes: Exact commands are in the textbook listings and in the PRG32 README.

## Slide 13
02
Two targets, two directories
Same source, different chips

## Slide 14: The two reference targets
 | Physical board | QEMU emulator
Chip | ESP32-C6 | ESP32-C3 (emulated)
Build directory | build-esp32c6 | build-qemu
Display | ILI9341 over SPI | Virtual RGB panel in a window
Input | Joystick and buttons | Keyboard, read from the terminal
Sound | I2S amplifier | Host audio, sent over a virtual UART
Cartridges arrive by | Wi-Fi upload | Staging into the flash image

## Slide 15: Why a C3 emulates for a C6
1
Both are RV32 microcontrollers from the same family
2
Espressif maintains a QEMU graphics path for the ESP32-C3
3
The physical kits use the newer ESP32-C6
4
The calling convention and the PRG32 interface are identical on both

## Slide 16: Keep the build directories strictly separate
1
build-qemu targets a virtual display that does not exist on hardware
2
Flashing it to a board gives a black screen
3
If the board shows nothing, check the build directory first
4
The prg32 tool chooses the right directory for you: use it

## Slide 17: Check your understanding
Your board shows a black screen after flashing. First thing to check?
A
The Wi-Fi password
B
That you flashed the build-esp32c6 image, not build-qemu
C
The cartridge RAM profile
D
The Python version
Notes: Answer: B. The QEMU build drives a virtual panel.

## Slide 18
03
The prg32 tool
One Python module for firmware, cartridges, and the Store

## Slide 19: Firmware commands
Command | Purpose
python3 -m prg32 doctor | Check the toolchain and partition table
python3 -m prg32 esp32c6 build-and-flash | Build and flash the board firmware
python3 -m prg32 qemu build | Build the emulator firmware and flash image
python3 -m prg32 qemu run | Start the emulator and its virtual screen
python3 -m prg32 wifi set --ssid ... --mode sta | Preconfigure the board's Wi-Fi

## Slide 20: Cartridge commands
Command | Purpose
cartridge build SRC --portable ... | Compile and package a .prg32
cartridge summary FILE | Print header, ABI, sizes, features
qemu upload FILE | Stage a cartridge into the emulator
esp32c6 upload FILE --url http://192.168.4.1 | Send a cartridge to a board over Wi-Fi
esp32c6 screenshot | Capture the board's screen
Notes: All are sub-commands of python3 -m prg32.

## Slide 21: A real build log
[INFO] Portable: True
[INFO] Building cartridge: work/hello/hello (Prefix: hello_world)
[INFO] Cartridge RAM limit: 65536 bytes (default firmware profile)
[OK] built work/hello/hello.prg32 name=hello load=0x40800000
[INFO] code=2664 mem=2664 audio=0
1
Portable: ABI-table imports
2
The 64 KiB profile limit
3
Load address of cartridge RAM
4
code: bytes copied; mem: bytes reserved (code + data + .bss)
Notes: Captured from a real build.

## Slide 22: What the builder does
Stage | Tool | Result
Compile | riscv32-esp-elf-gcc -march=rv32imac -mabi=ilp32 | game.o
C only | -Os -ffreestanding -fno-builtin -mcmodel=medany | small, position-tolerant code
Stubs | generated portable_stubs.S | 139 ABI stubs + 3 trampolines
Link | generated linker script at 0x40800000 | game.elf
Package | header + payload + CRC32 | game.prg32
Notes: From prg32/cartridge/build_cartridge.py.

## Slide 23: Flash once, upload often
Build firmware
once per course
Flash board
once
Build cartridge
seconds
Upload or stage
seconds
Play
and repeat
The resident firmware stays on the board. Your edit-build-run loop touches only the cartridge.

## Slide 24: The build command, option by option
python3 -m prg32 cartridge build work/hello/hello.S \
--portable \
--entry-prefix hello \
--name hello \
--out work/hello/hello.prg32
1
--portable: use the ABI table. Always.
2
--entry-prefix: must match your three function names
3
--name: what the menu shows
4
--out: the cartridge file

## Slide 25: QEMU reads the keyboard from the terminal
1
Click the terminal that launched QEMU, not the screen window
2
Arrows or W A S D move; Z or J is A; X or K is B
3
Enter or Space is Start/Select
4
Close QEMU before staging a new cartridge

## Slide 26
04
Profiles and diagnosis
Limits you should recognise, errors you will meet

## Slide 27: Cartridge memory profiles
Profile | Cartridge RAM | Use
Classroom | 32 KiB | Optional; leaves more heap to the runtime
Extended (default) | 64 KiB | Board and QEMU
128 KiB | 128 KiB | Optional; large games on the physical board
Notes: cartridge build assumes 64 KiB unless you pass --cart-ram-kib. esp32c6 upload asks the board.

## Slide 28: Sizes you will actually see
1
Empty cartridge: 2604 bytes (stubs and trampolines)
2
Hello world with one text call: 2664
3
Complete Pong in assembly: 2984; in C: 2952
4
Breakout with bricks, score and sound: about 3.4 KiB
5
All of them use about 5% of the 64 KiB profile
5%
of the default budget
Notes: Sizes from the build logs of the lab steps.

## Slide 29: Five failures and their causes
Symptom | Cause | Fix
idf.py: command not found | ESP-IDF not active | Source export.sh
riscv32-esp-elf-gcc missing | ESP-IDF not active or not installed for the target | install.sh esp32c3,esp32c6
Flash fails on Linux | No serial permission | Add user to dialout; log out and in
Board: black screen | Wrong build directory | Rebuild in build-esp32c6
QEMU ignores keys | Wrong window focused | Click the terminal

## Slide 30: Ports and permissions
1
Linux: boards appear as /dev/ttyACM0 or /dev/ttyUSB0
2
Linux: join the dialout group, then log out and back in
3
Windows: find the COM port in Device Manager; pass -p COMx
4
Only one program can hold a serial port: close other monitors

## Slide 31: Do you need all this?
Yes, to build
Writing assembly or C cartridges
Building or modifying firmware
Measuring performance on a board
No, to run or to start
Playing and debugging: PRG32-QT
Blocks: a browser and the Construction Kit
Reading code: the repository

## Slide 32: Check your understanding
Which command stages a cartridge into the emulator?
A
python3 -m prg32 esp32c6 upload
B
python3 -m prg32 qemu upload
C
python3 -m prg32 qemu build
D
idf.py flash
Notes: Answer: B. QEMU has no Wi-Fi path; cartridges are written into its flash image.

## Slide 33: Checkpoint
1
prg32 doctor passes in an ESP-IDF shell
2
You can say which chip and directory each target uses
3
You can read every option of cartridge build
4
You know where QEMU reads the keyboard
5
You can name the default cartridge RAM size

## Slide 34: Next steps and reading
Before the next session
Do the setup lab; bring your own laptop
Windows users: run the ESP-IDF installer before the lab
Read docs/usage/troubleshooting.md
Reading and sources
Textbook, Chapter 3
PRG32 README: Install and Setup
PRG32 docs/usage: getting_started, tooling, qemu, profiles
Espressif ESP-IDF documentation