## Slide 1
CHAPTER 5 | LECTURE | 45 MINUTES
First Contact: Registers, Memory, and the Call
The RV32 machine model, the first instructions, the stack frame, and state in .data
Audience: computer architecture students (RISC-V assembly track)
Playing with RISC-V: Assembly, C, and Retro Games on the PRG32 Platform
Notes: Teaching support for Chapter 5 of the textbook. Front lecture: about 45 minutes including the questions.

## Slide 2: Learning objectives
1
Describe the RV32 programmer's model: 32 registers, pc, memory
2
Name the register roles of the calling convention
3
Read and write arithmetic, load, store, and pseudo-instructions
4
Explain why ra must be saved before a nested call
5
Lay out a program in .text, .data, and .rodata
6
Trace a load-modify-store sequence by hand
Notes: State the objectives; return to this slide at the end.

## Slide 3: Agenda
8'
5'
10'
10'
7'
5'
1
The machine
2
The smallest program
3
Instructions
4
The call and the stack frame
5
Sections and memory
6
A program that ticks
Notes: Total: 45 minutes.

## Slide 4
A processor does three things: it computes in registers, it moves data to and from memory, and it decides where to go next.
Every instruction you will ever read is one of those three.

## Slide 5: The machine you are programming
1
32 registers
x0 to x31, each 32 bits wide. x0 is hard-wired to zero.
2
Program counter
pc holds the address of the next instruction.
3
Memory
A long array of bytes, addressed by 32-bit numbers. Words are 4 bytes, little-endian.
4
RV32IMAC
Base integer set, multiply/divide, atomics, compressed 16-bit encodings.

## Slide 6: Registers by role (ABI names)
Register | Role | Preserved by a call?
a0 - a7 | Arguments; a0 also the return value | No
t0 - t6 | Temporaries | No
s0 - s11 | Saved values | Yes
ra | Return address | No: save it yourself
sp | Stack pointer | Yes; keep 16-byte aligned
zero | Always 0 | -

## Slide 7: Why names instead of numbers
1
x10 and a0 are the same register
2
The names record a promise, the calling convention
3
The hardware does not enforce it; every compiler and every library relies on it
4
Break it and your program fails somewhere far from the mistake

## Slide 8: Check your understanding
Which register may a function you call freely overwrite?
A
s0
B
sp
C
t0
D
None
Notes: Answer: C. Temporaries (t0-t6) and argument registers are caller-saved; s registers and sp are preserved.

## Slide 9
01
The smallest program
Three labels that return

## Slide 10: A cartridge that does nothing, correctly
.option norelax
.section .text
.global hello_init
.global hello_update
.global hello_draw
hello_init:
ret # return to the framework
hello_update:
ret
hello_draw:
ret
1
.section .text: what follows is code
2
.global: export the name to the linker
3
A label names an address
4
ret jumps to the address in ra
Notes: Source: examples/asm_first_contact/hello_world_asm.S

## Slide 11: What the runtime does with it
Load
copy code to 0x40800000
call init
once
call update
every frame
call draw
every frame
The cartridge header stores the offsets of your three labels. 'call' places the return address in ra; your 'ret' uses it.

## Slide 12
02
Instructions
Compute, load, store

## Slide 13: Arithmetic and bit operations
Instruction | Meaning | Example
add rd, rs1, rs2 | rd = rs1 + rs2 | add t2, t2, t4
addi rd, rs1, imm | rd = rs1 + constant | addi t1, t1, 1
sub rd, rs1, rs2 | rd = rs1 - rs2 | sub t0, t1, t2
andi rd, rs1, imm | rd = rs1 AND constant | andi t3, t0, 1
slli rd, rs1, n | rd = rs1 shifted left n bits | slli t0, t0, 2
Notes: The immediate of addi is 12 bits, signed: -2048 to 2047.

## Slide 14: There is no subi
1
addi with a negative constant subtracts
2
addi t1, t1, -1 decrements t1
3
A small, regular instruction set is the R in RISC
4
Fewer instruction kinds make simpler, faster hardware

## Slide 15: addi t1, t1, 1 as 32 bits
31..20
imm[11:0]
000000000001
12 bit
19..15
rs1
00110 (t1 = x6)
5 bit
14..12
funct3
000
3 bit
11..7
rd
00110 (t1 = x6)
5 bit
6..0
opcode
0010011
7 bit
I-type: 0x00130313. The 12-bit immediate is signed, hence the range -2048..2047 and the lack of a subi. With the C extension the assembler may choose a 16-bit form instead.

## Slide 16: sw t1, 0(t0) as 32 bits
31..25
imm[11:5]
0000000
7 bit
24..20
rs2
00110 (t1)
5 bit
19..15
rs1
00101 (t0 = x5)
5 bit
14..12
funct3
010
3 bit
11..7
imm[4:0]
00000
5 bit
6..0
opcode
0100011
7 bit
S-type: 0x0062A023. The immediate is split so that rs1 and rs2 sit in the same bit positions in every format: simpler decoding hardware.

## Slide 17: Load and store word
Instruction | Meaning
lw rd, off(rs1) | rd = the 32-bit word at address rs1 + off
sw rs2, off(rs1) | the word at address rs1 + off = rs2
lb / lbu, lh / lhu | Load a byte or half-word, signed or unsigned
sb, sh | Store a byte or half-word
Notes: Memory is reached only through loads and stores. Arithmetic works only on registers.

## Slide 18: Pseudo-instructions
You write | The assembler emits | Purpose
li t0, 440 | addi, or lui + addi | Load a constant
la t0, label | auipc + addi | Load an address
mv t0, a0 | addi t0, a0, 0 | Copy a register
call f | auipc + jalr (sets ra) | Call a function
ret | jalr zero, 0(ra) | Return
neg t1, t1 | sub t1, zero, t1 | Negate

## Slide 19: Check your understanding
What does 'la t0, counter' put in t0?
A
The value stored in counter
B
The address of counter
C
The size of counter
D
Zero
Notes: Answer: B. la loads an address. A following lw fetches the value.

## Slide 20
03
The call
Why every non-trivial function begins and ends the same way

## Slide 21: What 'call' does to ra
1
Before
ra holds the address in the framework where your function must return.
2
call helper
ra is overwritten with the address just after the call.
3
helper returns
Execution continues in your function. ra still points into your function.
4
Your ret
Jumps to ra: back into yourself. An endless loop.
Notes: Unless you saved the original ra first.

## Slide 22: The stack frame: prologue and epilogue
print_init:
addi sp, sp, -16 # make 16-byte frame (keep sp 16-aligned)
sw ra, 12(sp) # save return address into the frame
call prg32_console_clear # clear text console (C helper)
la a0, title # put address of string in a0 (1st argument)
call prg32_console_write # print it
lw ra, 12(sp) # restore the return address
addi sp, sp, 16 # tear down the frame
ret # now ret goes to the right place
1
Make room: 16 bytes keeps sp aligned
2
Save ra into the frame
3
Now calls are safe
4
Restore ra, release the frame, return
Notes: Source: examples/asm_first_contact/print_asm.S

## Slide 23: The 16-byte frame in memory
+0
(free)
4 bytes
sp + 0
+4
(free)
4 bytes
sp + 4
+8
saved s0, if used
4 bytes
sp + 8
+12
saved ra
4 bytes
sp + 12
The stack grows toward lower addresses. sp must be a multiple of 16 at every call; that is why a function that needs 4 bytes still reserves 16.

## Slide 24: Two failures, reproduced
Mistake | What the host reports
ra not saved in a function that calls | frame 0: instruction budget exhausted (returns into itself forever)
sp restored by 8 instead of 16 | frame 0: instruction fetch outside cartridge memory (the caller reloads the wrong ra)
Notes: Both from running deliberately broken versions of the Lab 1 cartridge in the PRG32-QT headless runner.

## Slide 25: Rules of the frame
1
The stack grows downward: allocating subtracts from sp
2
Allocate in multiples of 16 bytes
3
Save ra if you call anything
4
Save any s register you use, and restore it
5
Every path out of the function must restore and release
16
bytes: stack alignment

## Slide 26: Arguments travel in a0, a1, a2...
la a0, title # 1st argument: address of the string
call prg32_console_write
li a0, 440 # 1st argument
li a1, 60 # 2nd argument
li a2, 512 # 3rd argument
call prg32_buzzer_tone
call prg32_input_read # result comes back in a0
1
First argument in a0, second in a1, ...
2
The return value arrives in a0
3
After a call, assume a and t registers are destroyed

## Slide 27: Check your understanding
A function calls a helper but never saves ra. What happens at its ret?
A
It returns normally
B
It jumps back to just after its own call: an endless loop or a crash
C
The assembler reports an error
D
The stack overflows at once
Notes: Answer: B. The call overwrote ra.

## Slide 28
04
Sections and memory
Where code, constants, and variables live

## Slide 29: The anatomy of a program
Section | Holds | Typical directives
.text | Instructions | .global, labels
.data | Variables with initial values | .word 0
.rodata | Constants that never change | .asciz "HELLO"
.bss | Variables that start at zero | .space 24
Notes: Initialised variables in a cartridge live in .data.

## Slide 30: Where a cartridge lands
Region | Address | Holds
External flash | 0x42000000 ... | firmware code and constants
HP SRAM | 0x40800000 - 0x4087FFFF | 512 KB: heap, firmware data, cartridge RAM
Cartridge | from 0x40800000 | .text, then .rodata, .data, .bss
LP SRAM | 0x50000000 ... | 16 KB kept in deep sleep
Notes: Cartridge code executes from RAM. Source: PRG32 docs/hardware/memory.md.

## Slide 31: State is memory with a name
.section .data
hello_x: .word 20 # object x position, in text columns
hello_score: .word 0 # a simple counter
1
.word reserves 4 bytes and sets their initial value
2
The label is the address of those bytes
3
Game state is exactly this: named words in .data
Notes: Source: examples/asm_first_contact/game_state_data.S

## Slide 32: Load, modify, store
la t0, hello_x # t0 = ADDRESS of hello_x
lw t1, 0(t0) # t1 = VALUE stored at that address
addi t1, t1, 1 # change the value (in the register)
sw t1, 0(t0) # write the new value back to memory
1
la: the address into t0
2
lw: memory to register
3
addi: compute in the register
4
sw: register back to memory
Notes: The single most important pattern of the track. Have students say it aloud. Source: examples/asm_first_contact/load_modify_store.S

## Slide 33: Why three steps to add one
1
RISC-V arithmetic never touches memory directly
2
This load-store design keeps each instruction simple and fast
3
The value in the register is a copy
4
Forgetting sw is the classic bug: the variable never changes

## Slide 34
05
A program that ticks
All of it together

## Slide 35: counter: one tick per frame
counter_update:
addi sp, sp, -16
sw ra, 12(sp) # save return address
la t0, counter
lw t1, 0(t0)
addi t1, t1, 1 # count one tick per frame
sw t1, 0(t0)
lw ra, 12(sp) # load return address
addi sp, sp, 16
1
Prologue
2
Load-modify-store on counter
3
Epilogue
4
Runs once per frame: the counter measures time in frames
Notes: Source: examples/asm_first_contact/counter.S

## Slide 36: Checkpoint
1
Name the role of a0, t0, s0, ra, sp
2
Explain what la, lw, and sw each do
3
Write a prologue and an epilogue from memory
4
Say why ra must be saved
5
Say in which section a variable and a string belong

## Slide 37: Next steps and reading
Before the next session
Lab: build print and counter; break and repair the frame
Read Chapter 6: branches and input
Correct your annotated listing from the orientation lab
Reading and sources
Textbook, Chapter 5
RISC-V unprivileged ISA specification
PRG32 docs/software/abi.md
PRG32 docs/learn/tutorial_ascii_game.md