## Slide 1
MAKER FAIRE | WORKSHOP | 2.5 HOURS | THREE PARTS OF 20' + 30'
The One When Future Tech Is Tough: Mastering Retro Games with PRG32
A retro game development platform for learning and mastering the European RISC-V processor
Audience: students, makers, electronics enthusiasts, hobbyist programmers, educators
High Performance Scientific Computing SmartLab - University of Naples "Parthenope"
Notes: Workshop for 15-30 participants in pairs: 30 PRG32 kits, 15 preconfigured laptops (PRG32 checkout, ESP-IDF active, PRG32_HOME set, this folder copied). Each kit runs its own Wi-Fi network; set PRG32_URL=http://192.168.4.1 on the laptop joined to it. Every step is a complete file started with ./run.sh PART STEP. All screenshots in the slides come from actually building and running that step.

## Slide 2: Learning objectives
1
Understand the fundamentals of the RISC-V instruction set
2
Write simple assembly programs
3
Interface software with graphics, controllers and audio
4
Understand how C and assembly cooperate
5
Build and run a complete retro game cartridge
Notes: State the objectives; return to this slide at the end.

## Slide 3: Plan of the session
20'
30'
20'
30'
20'
30'
1
Part 1: welcome to the PRG32 universe
2
Hands-on: your first cartridge
3
Part 2: programming games in assembly
4
Hands-on: a game in assembly
5
Part 3: from assembly to C
6
Hands-on: C and assembly together
Notes: Total: 150 minutes.

## Slide 4
01
Part 1: welcome to the PRG32 universe
Presentation, 20 minutes

## Slide 5
What do retro video games have in common with Europe's future processors?
Both reward people who know what really happens inside the machine.

## Slide 6: Why RISC-V matters
Proprietary architectures
The instruction set belongs to a company
Building a processor needs a licence
The roadmap is decided elsewhere
RISC-V
An open standard, born at Berkeley
Anyone may design a processor
Extensible by design
From microcontrollers to supercomputers

## Slide 7: The European open hardware ecosystem
Fact | Figure
Global semiconductor market | about 700 billion USD
Europe's current share | about one tenth
European Chips Act target | one fifth by 2030
DARE (EuroHPC): European processors on RISC-V | about 240 million EUR
Notes: Orders of magnitude as cited in the textbook (HiPEAC 2026, EuroHPC JU). Keyword: digital sovereignty.

## Slide 8: The PRG32 educational philosophy
1
Learning by making
No theory lecture first: build it, then understand why it works.
2
Immediate feedback
Every instruction produces something on screen. If it is wrong, you can see it.
3
Incremental challenges
One thing at a time: every step is a complete program that works.
4
In pairs
One drives, one reads; swap at every step.

## Slide 9: Why a retro console
1
8-bit consoles were simple enough to understand completely
2
A few kilobytes, a few colours: constraints force understanding
3
A game contains everything: state, input, arithmetic, decisions, time
4
PRG32 brings that simplicity back on a modern, open processor

## Slide 10: The PRG32 hardware
Component | Details
ESP32-C6 | RISC-V RV32IMAC at 160 MHz, 512 KB RAM, Wi-Fi
ILI9341 display (SPI) | 320 x 240, RGB565; games use 320 x 200
Joystick and buttons (GPIO) | 4 directions, A, B, Start/Select
Audio (I2S) | MAX98357A; 8-voice mixer, 22,050 Hz
Cartridge memory | 64 KiB; our games use about 3

## Slide 11: Memory-mapped hardware
1
To the processor, a peripheral is a memory address
2
Reading buttons = reading a register: each button is one bit
3
Drawing = writing numbers into an area of memory, the framebuffer
4
The PRG32 runtime does those reads and writes for us, behind 139 functions
5
That is why input arrives as a bit mask
64,000
bytes of framebuffer: one byte per pixel

## Slide 12: The development workflow
Source
.S or .c
RISC-V toolchain
on the laptop
Cartridge
.prg32 file
Wi-Fi
to the kit
init / update / draw
the game runs
The firmware stays on the console. Only the cartridge is rebuilt and uploaded: a few seconds per iteration.

## Slide 13: The cartridge
+0
PRG2
4 bytes
format signature
+4
ABI version
4 bytes
which function table it expects
+8
sizes, address
16 bytes
where to load it and how large it is
+24
init / update / draw
12 bytes
the game's entry points
+36
CRC32
4 bytes
integrity
+40
name
32 bytes
what the menu shows
+72
ABI hash, required features
28 bytes
an incompatible cartridge is refused
code and data
~3 KiB
RISC-V instructions: ours
A 100-byte header. Of those 3 KiB, about 2.5 are the 139 small stubs that reach the console's functions.

## Slide 14: Assembly language fundamentals
Instruction | What it does
li a0, 5 | puts 5 in register a0
la t0, x | puts the address of x in t0
lw t1, 0(t0) | loads a word from memory
addi t1, t1, 1 | t1 = t1 + 1
sw t1, 0(t0) | stores a word to memory
call f / ret | calls f / returns
Notes: Compute, move, decide: there is nothing else.

## Slide 15: An instruction is a 32-bit number
31..20
immediate
000000000001
12 bit
19..15
rs1
00110 (t1)
5 bit
14..12
funct3
000
3 bit
11..7
rd
00110 (t1)
5 bit
6..0
opcode
0010011
7 bit
addi t1, t1, 1 in its 32-bit form is 0x00130313. RISC-V also has 16-bit compressed forms of the most common instructions.
Notes: I-type: imm=1, rs1=x6, funct3=0, rd=x6, opcode=0x13.

## Slide 16
02
Hands-on 1: your first cartridge
30 minutes, in pairs

## Slide 17: Explore the environment
1
Power the PRG32 kit and join the laptop to its Wi-Fi network
2
export PRG32_URL=http://192.168.4.1
3
cd workshops/Maker_Faire && ls part1 part2 part3
4
From the PRG32 folder run: python3 -m prg32 doctor
Step 1
about 5 min
Expected result
Three folders of steps. doctor reports OK for the ESP-IDF toolchain, the RISC-V compiler, and the partition table.

## Slide 18: Step 1.2: text on the screen
hello_world_draw:
addi sp, sp, -16
sw ra, 12(sp) # this function calls others: save ra
li a0, BLACK
call prg32_gfx_clear
li a0, 32 # x
li a1, 40 # y
la a2, title # address of the string
li a3, CYAN # foreground colour
li a4, BLACK # background colour
call prg32_gfx_text8
lw ra, 12(sp)
Screenshot: this step, built and run
Three exported labels; draw saves ra, clears the screen and writes a string with five arguments in a0..a4.
Notes: Source: workshops/Maker_Faire/part1/step2_text.S

## Slide 19: Build and run
1
./run.sh 1 1
2
./run.sh 1 2
3
Read the code_size printed by the script
4
Change the text and its x, y; run again
Step 2 | about 8 min
Expected result
Step 1: a black screen. Step 2: HELLO WORLD in cyan. code_size about 2660 bytes.
Notes: Screenshot: this step, built and run: workshops/Maker_Faire/part1/expected/step2_text.png

## Slide 20: Modify text and graphics
1
./run.sh 1 3
2
Change CYAN to 0xF800 (red) in its .equ line
3
Compute an RGB565 colour yourself: 5 bits red, 6 green, 5 blue
4
Add a third line of text 24 pixels lower
Step 3 | about 7 min
Expected result
Two lines of text; then three, in your colours.
Notes: Screenshot: this step, built and run: workshops/Maker_Faire/part1/expected/step3_two_lines.png

## Slide 21: Step 1.4: a sprite and a button
# An 8x8 sprite: one byte per row, one bit per pixel.
li a0, 152 # x
li a1, 96 # y
la a2, ship # address of the 8 bytes
li a3, CYAN # foreground: cyan...
la t0, buttons
lw t1, 0(t0)
andi t1, t1, BTN_A
beqz t1, 1f
li a3, YELLOW # ...yellow while A is held
1: li a4, BLACK # background
call prg32_sprite_draw_8x8
Screenshot: this step, built and run
Eight bytes, one bit per pixel. andi isolates the A button's bit: the sprite turns yellow while A is held.
Notes: Source: workshops/Maker_Faire/part1/step4_sprite_button.S

## Slide 22: Buttons and display
1
./run.sh 1 4
2
Hold A: the sprite changes colour
3
Change BTN_A (0x10) to 0x20: which button responds now?
4
Redraw the sprite: edit the eight bytes after 'ship:'
Step 4 | about 10 min
Expected result
A cyan sprite, yellow while A is held (screenshot). 0x20 is button B.
Notes: 0x18 = 00011000, 0xff = 11111111: draw the rows on squared paper first. Screenshot: this step, built and run: workshops/Maker_Faire/part1/expected/step4_sprite_button.png

## Slide 23
03
Part 2: programming games in assembly
Presentation, 20 minutes

## Slide 24: RISC-V registers
Register | Role | Survives a call?
a0 - a7 | arguments; a0 also the result | no
t0 - t6 | temporaries | no
s0 - s11 | saved values | yes
ra | return address | no: save it yourself
sp | stack pointer | yes; 16-byte aligned

## Slide 25: Functions and the calling convention
1
Prologue
addi sp, sp, -16
sw ra, 12(sp)
2
Arguments
in a0, a1, a2... in order
3
call
writes the return address into ra
4
Epilogue
lw ra, 12(sp)
addi sp, sp, 16
ret
Notes: Verified in the lab material: removing the ra save makes the cartridge loop forever; PRG32-QT reports 'instruction budget exhausted'.

## Slide 26: Conditions and loops
A condition is a forward branch
andi t3, a0, 1
beqz t3, 1f
addi t2, t2, -4
1:
A loop is a backward branch
li s0, 0
loop: ...
addi s0, s0, 1
blt s0, t0, loop
Notes: The branch tests the opposite condition and jumps over the body.

## Slide 27: Sprites and rectangles
1
prg32_gfx_rect(x, y, w, h, color): five registers
2
prg32_sprite_draw_8x8(x, y, bits, foreground, background)
3
prg32_sprite_hitbox: eight arguments, answers whether two rectangles overlap
4
Coordinates come from state; sizes are constants

## Slide 28: Input is a bit mask
Button | Value | Binary
LEFT | 0x01 | 0000 0001
RIGHT | 0x02 | 0000 0010
UP | 0x04 | 0000 0100
DOWN | 0x08 | 0000 1000
A | 0x10 | 0001 0000
B | 0x20 | 0010 0000
Notes: andi isolates one bit; beqz skips when it is zero. Never compare with ==: several buttons may be held.

## Slide 29: Timing: the game loop
init
once
read input
buttons
update
change state
draw
render state
About 30 frames per second: 33 ms for update plus draw. A speed of 2 means 2 pixels per frame, 60 pixels per second.

## Slide 30: Motion: position plus velocity
1
Two numbers per axis: position and signed velocity
2
Every frame: x = x + dx
3
At an edge: clamp to the edge and flip the sign (neg)
4
Limit = screen size minus object size
320 - 8
= 312

## Slide 31
04
Hands-on 2: a game in assembly
30 minutes: movement, collisions, scoring, sound

## Slide 32: Step 2.2: player movement
# --- paddle: move with LEFT / RIGHT, clamp to the screen
la t1, paddle_x
lw t2, 0(t1)
andi t3, a0, 1 # LEFT
beqz t3, 1f
addi t2, t2, -PADDLE_SPEED
1: andi t3, a0, 2 # RIGHT
beqz t3, 2f
addi t2, t2, PADDLE_SPEED
2: bgez t2, 3f
li t2, 0
3: li t3, PADDLE_MAX
ble t2, t3, 4f
mv t2, t3
Screenshot: this step, built and run
Load, modify, store. Two bit tests, then two checks keep the paddle between 0 and 256.
Notes: Source: workshops/Maker_Faire/part2/step2_move.S

## Slide 33: Try the movement
1
./run.sh 2 1
2
./run.sh 2 2
3
Hold RIGHT up to the edge
4
Change PADDLE_SPEED from 4 to 12
Step 5 | about 5 min
Expected result
The paddle follows the joystick and stops at x = 256 (screenshot: RIGHT for 30 frames).
Notes: Screenshot: this step, built and run: workshops/Maker_Faire/part2/expected/step2_move.png

## Slide 34: Step 2.3: the ball
# --- ball x: add velocity, bounce off the side walls
la t1, ball_x
lw t2, 0(t1)
la t3, ball_dx
lw t4, 0(t3)
add t2, t2, t4 # x = x + dx
bgez t2, 5f
li t2, 0 # clamp to the left edge
neg t4, t4 # and reverse
5: li t5, BALL_MAX_X
ble t2, t5, 6f
mv t2, t5 # clamp to the right edge
neg t4, t4
6: sw t2, 0(t1)
Screenshot: this step, built and run
x = x + dx; at each side wall the ball is clamped to the edge and dx is flipped with neg.
Notes: Source: workshops/Maker_Faire/part2/step3_ball.S

## Slide 35: Step 2.4: collision detection
# --- paddle collision
la t0, ball_x
lw a0, 0(t0) # a0..a3: the ball rectangle
la t0, ball_y
lw a1, 0(t0)
li a2, BALL_SIZE
li a3, BALL_SIZE
la t0, paddle_x
lw a4, 0(t0) # a4..a7: the paddle rectangle
li a5, PADDLE_Y
li a6, PADDLE_W
li a7, PADDLE_H
call prg32_sprite_hitbox # a0 = non-zero if they overlap
beqz a0, update_done
la t0, ball_dy
lw t1, 0(t0)
blez t1, update_done # guard: bounce only while moving down
neg t1, t1
sw t1, 0(t0)
Screenshot: this step, built and run
Ball in a0-a3, paddle in a4-a7. blez: bounce only while moving down, so one hit counts once.
Notes: Source: workshops/Maker_Faire/part2/step4_collision.S

## Slide 36: Try ball and collision
1
./run.sh 2 3
2
./run.sh 2 4
3
Keep the ball alive for five bounces
4
Delete the blez line and hit the ball from the side; then restore it
Step 6 | about 8 min
Expected result
With step 4 the paddle returns the ball; without blez the ball can jitter inside the paddle.
Notes: Screenshot: this step, built and run: workshops/Maker_Faire/part2/expected/step4_collision.png

## Slide 37: Step 2.5: scoring
# --- score: a bar 4 pixels long per point, at most 312
la t0, score
lw t1, 0(t0)
slli a2, t1, 2 # width = score * 4
li t2, 312
ble a2, t2, 1f
mv a2, t2
1: li a0, 4
li a1, 4
li a3, 6
li a4, GREEN
call prg32_gfx_rect
Screenshot: this step, built and run
New state (score), new rule (+1 inside the guard), new picture: a bar score x 4 wide, using slli.
Notes: Source: workshops/Maker_Faire/part2/step5_score.S

## Slide 38: Step 2.6: sound effects
li a0, 0 # channel
li a1, 0 # instrument
li a2, 72 # MIDI note 72 = C5
li a3, 255 # volume
li a4, 60 # milliseconds
call prg32_audio_note # t registers are dead after this call
Screenshot: this step, built and run
prg32_audio_note(channel, instrument, MIDI note, volume, ms). After the call the t registers are dead.
Notes: Source: workshops/Maker_Faire/part2/step6_sound.S

## Slide 39: Try scoring and sound
1
./run.sh 2 5
2
./run.sh 2 6
3
Change note 72 to 84, then to 60
4
Make the bar grow 8 pixels per point: which instruction changes?
Step 7 | about 10 min
Expected result
A growing green bar and a note at every bounce. slli a2, t1, 3 multiplies by 8.
Notes: Screenshot: this step, built and run: workshops/Maker_Faire/part2/expected/step6_sound.png

## Slide 40
05
Part 3: from assembly to C
Presentation, 20 minutes

## Slide 41: Why combine C and assembly
C for structure
Variables, arrays, loops in a few lines
Readable by others
The compiler chooses registers and stack
Almost all of the game
Assembly where it matters
Exact control of what executes
Small, critical routines
Access to special instructions
Understanding what the compiler does

## Slide 42: The same rule, two languages
C | Assembly
input = prg32_input_read(); | call prg32_input_read
if (input & PRG32_BTN_LEFT) | andi t3, a0, 1 / beqz t3, 1f
paddle_x -= 4; | lw / addi -4 / sw
prg32_gfx_rect(x, y, w, h, c); | a0..a4, call prg32_gfx_rect
Notes: C does not hide the machine: it describes it more comfortably.

## Slide 43: Where they meet: the calling convention
1
A C function and an assembly routine are the same thing to the processor
2
Arguments in a0, a1, a2...; result in a0
3
A C pointer (&ball_x) is an address in a register
4
The callee preserves s0-s11 and sp
5
One C declaration is enough: int ball_step_asm(int *, int *, int);

## Slide 44: The PRG32 runtime
Your cartridge
C + assembly
Stubs
139 entries
ABI table
version 1.6
Firmware
display, input, audio
ESP32-C6
RISC-V
The cartridge does not know the firmware's addresses: it calls entry number N of a table. That is why the same file runs on the board, in QEMU and in PRG32-QT.

## Slide 45: Inside a stub
prg32_gfx_rect: # one of 139 generated stubs
la t0, __prg32_abi # where the table pointer was saved
lw t0, 0(t0) # t0 = address of the ABI table
lw t1, 104(t0) # t1 = table entry for this function
jr t1 # jump there; arguments untouched in a0..a7
prg32_entry_update: # what the console really calls
addi sp, sp, -16
sw ra, 12(sp)
la t0, __prg32_abi
sw a0, 0(t0) # the console passes the table in a0
call pong_update # your function
lw ra, 12(sp)
addi sp, sp, 16
ret
1
Generated by the cartridge builder
2
A few instructions per function
3
Your update is called through a trampoline
Notes: Shape of the code emitted by prg32/cartridge/build_cartridge.py; the offset shown (104) is illustrative: 20 + index * 4.

## Slide 46: Modular game architecture
1
State
A few named variables: all the game remembers.
2
Rules
update: small functions, one responsibility each.
3
Rendering
draw: reads state, never changes it.
4
Fast modules
Assembly routines behind a C declaration.

## Slide 47: Cartridge packaging
1
python3 -m prg32 cartridge build SOURCE --portable --entry-prefix ...
2
cartridge summary: sizes, ABI, import model
3
esp32c6 upload-and-run --url ...: to the kit over Wi-Fi
4
Optional: icon, credits and publication on the Cartridge Store

## Slide 48
06
Hands-on 3: C and assembly together
30 minutes: migrate, integrate, complete, exchange

## Slide 49: Step 3.1: the assembly module
__asm__(
" .text\n"
" .globl ball_step_asm\n"
"ball_step_asm:\n"
" lw t0, 0(a0)\n" /* t0 = *position (a0 = 1st argument) */
" lw t1, 0(a1)\n" /* t1 = *velocity (a1 = 2nd argument) */
" add t0, t0, t1\n" /* position += velocity */
" li t2, 0\n" /* t2 = bounced? no */
" bgez t0, 1f\n"
" li t0, 0\n" /* below 0: clamp... */
" neg t1, t1\n" /* ...and reverse */
" li t2, 1\n"
"1: ble t0, a2, 2f\n" /* a2 = max (3rd argument) */
" mv t0, a2\n"
" neg t1, t1\n"
" li t2, 1\n"
"2: sw t0, 0(a0)\n"
" sw t1, 0(a1)\n"
" mv a0, t2\n" /* return value goes back in a0 */
Screenshot: this step, built and run
The ball physics stays in assembly: a0 and a1 are two addresses, a2 the limit, the result returns in a0.
Notes: Source: workshops/Maker_Faire/part3/step1_c_calls_asm.c

## Slide 50: Step 3.1: C calls assembly
void mixed_update(void) {
uint32_t input = prg32_input_read();
if (input & PRG32_BTN_LEFT) { paddle_x -= 4; }
if (input & PRG32_BTN_RIGHT) { paddle_x += 4; }
if (paddle_x < 0) { paddle_x = 0; }
if (paddle_x > PRG32_GAME_W - PADDLE_W) { paddle_x = PRG32_GAME_W - PADDLE_W; }
/* C calls assembly: pass two addresses and a limit */
ball_step_asm(&ball_x, &ball_dx, PRG32_GAME_W - BALL_SIZE);
ball_step_asm(&ball_y, &ball_dy, 100000); /* no floor: the ball can be lost */
if (ball_y >= PRG32_GAME_H) {
ball_x = 156;
ball_y = 120;
ball_dy = -2;
}
1
The paddle: four lines of C
2
&ball_x: the variable's address
3
Two calls to the same routine
4
The rest of the game is C
Notes: The cartridge builder takes one source file, so the assembly module is embedded as a top-level asm block in the C file. Source: workshops/Maker_Faire/part3/step1_c_calls_asm.c

## Slide 51: Migrate and integrate
1
./run.sh 3 1
2
Compare part3/step1_c_calls_asm.c with part2/step4_collision.S: same game
3
Count the lines of both files
4
In the assembly module change 'neg t1, t1' to 'li t1, 0' at the first edge: what happens?
Step 8 | about 10 min
Expected result
The same Pong, now in C with physics in assembly. With li t1, 0 the ball stops moving sideways at the left wall.
Notes: Screenshot: this step, built and run: workshops/Maker_Faire/part3/expected/step1_c_calls_asm.png

## Slide 52: Step 3.2: bricks, in C
/* in C a loop over an array is three lines */
for (int i = 0; i < BRICKS; i++) {
if (bricks[i] &&
prg32_sprite_hitbox(ball_x, ball_y, BALL_SIZE, BALL_SIZE,
brick_x(i), brick_y(i), 36, 10)) {
bricks[i] = 0;
ball_dy = -ball_dy;
break;
}
}
}
Screenshot: this step, built and run
An array of 16 bytes and a loop: what takes thirty instructions in assembly is ten lines of C.
Notes: Source: workshops/Maker_Faire/part3/step2_bricks.c

## Slide 53: Build the complete cartridge
1
./run.sh 3 2
2
./run.sh 3 3
3
Read code_size: how much did the cartridge grow since step 3.1?
4
Add a third row of bricks: BRICKS 24
Step 9 | about 10 min
Expected result
A complete Breakout: score, sound, win. About 3.3 KiB against 2.9 for step 3.1.
Notes: Screenshot: this step, built and run: workshops/Maker_Faire/part3/expected/step3_complete.png

## Slide 54: Test and exchange games
1
Customise: colours, speeds, paddle width
2
Your cartridge is build/part3-step3.prg32
3
Join your neighbours' kit Wi-Fi
4
python3 -m prg32 esp32c6 upload-and-run build/part3-step3.prg32 --url http://192.168.4.1 --slot cart1
Step 10
about 10 min
Expected result
Your game runs on another pair's kit, in slot cart1, next to theirs.
Notes: Run the command from the PRG32 folder with the full path to the cartridge, or copy the .prg32 file on a USB stick.

## Slide 55
07
Where to go from here
Future learning paths

## Slide 56: Four paths
1
The textbook
Playing with RISC-V: three tracks (assembly, C, blocks) with step-by-step labs.
2
The debugger
PRG32-QT stops the processor between two instructions and shows every register.
3
Publishing
The Cartridge Store: a reviewed catalogue, leaderboards, multiplayer.
4
Teaching
The Construction Kit brings the same game to children from age 7, with blocks.

## Slide 57: What you take home
1
You wrote and modified real RISC-V programs
2
You can read registers, branches, calls
3
You connected code to screen, buttons and audio
4
You made C and assembly cooperate
5
You built and exchanged a cartridge

## Slide 58: Next steps and reading
Before the next session
Every step is in workshops/Maker_Faire of the textbook repository
Redo the steps at home in QEMU or PRG32-QT: no kit needed
Build your own PRG32: ESP32-C6, ILI9341 display, joystick
Bring PRG32 to your school or makerspace
Reading and sources
PRG32: github.com/riscv-prg32/PRG32
Cartridge Store: store.prg32.uniparthenope.it
PRG32-QT, Construction Kit: github.com/riscv-prg32
Playing with RISC-V: github.com/riscv-prg32/Playing-with-RISC-V_PRG32_textbook
HPSC SmartLab, University of Naples "Parthenope"