## Slide 1
CHAPTER 2 | LABORATORY | 45 MINUTES
Design Lab: A Game on Paper
Decompose Pong into state, update rules, and draw calls before writing a line of code
Audience: first-year computer architecture and programming students
Playing with RISC-V: Assembly, C, and Retro Games on the PRG32 Platform
Notes: Teaching support for Chapter 2 of the textbook. Practical, step-by-step session: learners work at their machines; keep each step to its time box. Preparation: Squared paper, coloured pens. One printed 40 by 25 grid per pair. No computers needed until the last ten minutes.

## Slide 2: Learning objectives
1
Decompose a game into state variables and update rules
2
Place objects in the 320 by 200 coordinate system
3
Compute RGB565 values and input bitmasks by hand
4
Write init, update, and draw as structured pseudocode
5
Check a design against the three rules for first games
Notes: State the objectives; return to this slide at the end.

## Slide 3: Plan of the session
10'
10'
8'
12'
5'
1
State on paper
2
Coordinates and colour
3
Input bitmasks
4
Pseudocode for three functions
5
Review
Notes: Total: 45 minutes.

## Slide 4: Why design on paper first
1
A machine that is unforgiving rewards thinking before typing
2
Paper makes state visible: every variable gets a box
3
You will build exactly this design in your track's next chapters
4
Keep the sheets: they are the specification for your first game

## Slide 5
01
State
What must the game remember between frames?

## Slide 6: The game: one-player Pong
ball
paddle
320 x 200 game viewport
1
A paddle moves left and right
2
A ball bounces off walls and paddle
3
The ball restarts if it passes the paddle

## Slide 7: List the state
1
Draw one box for every number the game must remember
2
Name each box: paddle_x, ball_x, ball_y, ...
3
Write a starting value in each
4
Mark which ones never change: these are constants
Step 1
about 5 min
Expected result
At least paddle_x, ball_x, ball_y, ball_dx, ball_dy as variables; widths, heights, paddle_y, speeds as constants.

## Slide 8: One good answer
Name | Kind | Initial value | Changed by
paddle_x | variable | 130 | LEFT and RIGHT
ball_x, ball_y | variable | 150, 20 | velocity, every frame
ball_dx, ball_dy | variable | 2, 2 | bounces
PADDLE_Y | constant | 180 | never
PADDLE_W, PADDLE_H | constant | 60, 8 | never
BALL_SIZE | constant | 8 | never

## Slide 9: Check your understanding
Why is paddle_y a constant but paddle_x a variable?
A
y cannot be stored in a register
B
The paddle only moves horizontally in this design
C
Constants are faster to draw
D
The framework forbids changing y
Notes: Answer: B. State is exactly what changes between frames; everything else is a constant.

## Slide 10
02
Coordinates and colour
Arithmetic you should be able to do without a computer

## Slide 11: Place the objects
1
On squared paper, let one square be 8 by 8 pixels: the grid is 40 by 25
2
Draw the paddle at x 130, y 180, 60 wide, 8 high
3
Draw the ball at x 150, y 20
4
Mark the pixel coordinates of each corner of the paddle
Step 2
about 4 min
Expected result
Paddle corners at (130,180), (190,180), (130,188), (190,188). The right edge is x + w.

## Slide 12: Find the limits
1
What is the largest paddle_x that keeps a 60-wide paddle on screen?
2
What is the largest ball_y before an 8-high ball leaves the bottom?
3
Write both as formulas using the screen size
4
Check with your drawing
Step 3
about 4 min
Expected result
paddle_x max = 320 - 60 = 260. ball_y max = 200 - 8 = 192. In general: limit = screen size - object size.

## Slide 13: RGB565 by hand
1
Layout
RRRRR GGGGGG BBBBB: red in bits 15-11, green in 10-5, blue in 4-0.
2
Full red
11111 000000 00000 = 0xF800.
3
Full green
00000 111111 00000 = 0x07E0.
4
Yellow = red + green
11111 111111 00000 = 0xFFE0.

## Slide 14: Compute three colours
1
Write cyan (green + blue) in binary, then in hexadecimal
2
Write magenta (red + blue)
3
Write a half-brightness red: red field = 10000
4
Compare with the constants table
Step 4
about 5 min
Expected result
Cyan 0x07FF, magenta 0xF81F, half red 0x8000.

## Slide 15
03
Input
Bits in a register

## Slide 16: The bits you need
Button | Mask | Binary
LEFT | 0x01 | 0000 0001
RIGHT | 0x02 | 0000 0010
UP | 0x04 | 0000 0100
DOWN | 0x08 | 0000 1000
A | 0x10 | 0001 0000
B | 0x20 | 0010 0000

## Slide 17: Encode and decode
1
Write the value returned when RIGHT and B are held
2
Write the value for UP, LEFT, and A together
3
Decode 0x12: which buttons?
4
Decode 0x09: which buttons? Is that physically likely?
Step 5
about 4 min
Expected result
RIGHT+B = 0x22. UP+LEFT+A = 0x15. 0x12 = RIGHT and A. 0x09 = LEFT and DOWN (a diagonal).

## Slide 18: Write the tests
1
Write the expression that is true when LEFT is held
2
Write one that is true when A or B is held
3
Write one that is true only when LEFT and RIGHT are both held
4
Explain why == would be wrong in the first
Step 6
about 4 min
Expected result
input & 0x01; input & 0x30; (input & 0x03) == 0x03. Equality fails as soon as any other button is held.

## Slide 19
04
Three functions
Structured pseudocode: one step from real code

## Slide 20: A template to fill in
init:
set every variable to its starting value
update:
read input
move the paddle; keep it on screen
move the ball
bounce off walls
bounce off the paddle
restart the ball if it is lost
draw:
clear the screen
draw the paddle
draw the ball
1
update changes numbers only
2
draw calls the framework only
3
Each line becomes a few instructions or one C statement

## Slide 21: Write update in detail
1
Expand 'move the paddle' into if-statements using your masks
2
Expand 'keep it on screen' using your limits
3
Expand 'bounce off walls': which velocity changes sign at which edge?
4
Use only your named state and constants
Step 7
about 7 min
Expected result
Six to ten precise lines, such as: if input & LEFT then paddle_x = paddle_x - 4; if ball_x < 0 then ball_dx = -ball_dx.

## Slide 22: Write the paddle bounce
1
Which call tests whether two rectangles overlap?
2
List its eight arguments for ball and paddle, in order
3
What happens to ball_dy on a hit?
4
What could make one hit count several times?
Step 8
about 5 min
Expected result
prg32_sprite_hitbox(ball_x, ball_y, 8, 8, paddle_x, 180, 60, 8). On a hit ball_dy becomes negative. If the ball stays overlapped next frame it flips again: force the direction upward.

## Slide 23: Check your understanding
The ball sticks to the paddle and jitters. Most likely cause?
A
The paddle is drawn after the ball
B
ball_dy is negated on every overlapping frame
C
The ball is too small
D
The hitbox call is in draw
Notes: Answer: B. Set ball_dy to a negative value on a hit, do not negate it.

## Slide 24: Write draw
1
List the framework calls in order
2
Give every argument, using your state and constants
3
Which call must be first, and why?
Step 9
about 3 min
Expected result
prg32_gfx_clear(BLACK); prg32_gfx_rect(paddle_x, 180, 60, 8, CYAN); prg32_gfx_rect(ball_x, ball_y, 8, 8, WHITE). Clear first, or old frames remain.

## Slide 25
05
Review
Check the design against the rules

## Slide 26: Plan your build order
1
Skeleton
Three functions that return. Build and run.
2
Paddle visible
State, init, one rect in draw.
3
Paddle moves
Input and clamp in update.
4
Ball and bounces
Velocity, walls, then paddle.
Notes: This is the order the assembly and C tracks follow.

## Slide 27: Peer review
1
Swap designs with another pair
2
Find one variable they forgot or one limit that is off by one
3
Find one thing they did better than you
4
Return the sheet with both notes
Step 10
about 4 min
Expected result
Each design carries two written comments from another pair.

## Slide 28: Optional: see it run
1
Open PRG32-QT and run Pong from the Store
2
Hold LEFT until the paddle stops: does it stop where your limit says?
3
Watch a paddle bounce in 0.1x slow motion
Step 11
about 3 min
Expected result
The running game behaves as your paper design predicts, or you find out which of the two is wrong.

## Slide 29: You can now
1
Write a game's state as named variables and constants
2
Compute screen limits from sizes
3
Encode and decode the input bitmask
4
Express update and draw as ordered, separate steps
5
Plan an incremental build

## Slide 30: Next steps and reading
Before the next session
Bring your design sheets to the next lab
Install the toolchain (Chapter 3)
Assembly track: Chapter 5. C track: Chapter 9
Reading and sources
Textbook, Chapter 2
PRG32 docs/learn/tutorial.md
examples/games/pong in the PRG32 repository