## Slide 1
CHAPTER 2 | LECTURE | 45 MINUTES
Game Design Principles and the PRG32 Framework
The frame loop, the three-function contract, the screen, input, sound, and cartridges
Audience: first-year computer architecture and programming students
Playing with RISC-V: Assembly, C, and Retro Games on the PRG32 Platform
Notes: Teaching support for Chapter 2 of the textbook. Front lecture: about 45 minutes including the questions.

## Slide 2: Learning objectives
1
Describe a game as a loop over frames that reads, updates, and draws
2
State the three-function contract and why update and draw are separate
3
Use the coordinate system and RGB565 colours
4
Test a button in the input bitmask
5
Explain what a portable cartridge is and how it reaches the machine
6
Apply the three design rules for first games
Notes: State the objectives; return to this slide at the end.

## Slide 3: Agenda
8'
6'
8'
6'
4'
8'
5'
1
What a game is
2
The contract
3
Screen and colour
4
Input
5
Sound
6
Cartridges and targets
7
Design rules
Notes: Total: 45 minutes.

## Slide 4
A game is a loop that never ends until you tell it to.
Each turn of the loop is a frame: read, update, draw.

## Slide 5: The frame loop
init
once at start
read input
buttons, time
update
change state
draw
render state
State is the set of variables that describe the game right now: positions, velocities, scores. Every rule of the game turns this frame's state into the next frame's.

## Slide 6: Update and draw are kept apart on purpose
update
May change state
Must not draw
Movement, collisions, score
Testable without a screen
draw
May read state
Must not change game logic
Clear, then paint every object
Could be skipped without breaking rules
Notes: Mixing them produces bugs such as collisions detected only when an object happens to be drawn.

## Slide 7: The universal shape of a PRG32 game
<prefix>_init runs once when the cartridge is selected
<prefix>_update runs once per frame; changes game state
<prefix>_draw runs once per frame; renders the state
pong_graphics_init / _update / _draw (assembly)
pong_c_init / _update / _draw (C)
1
The prefix names the game
2
The framework does not care which language produced the symbols

## Slide 8: Check your understanding
Where does a collision test belong?
A
In init
B
In update
C
In draw
D
In both update and draw
Notes: Answer: B. Collisions change state, so they belong to update.

## Slide 9
01
The screen
Coordinates, the viewport, and colour

## Slide 10: The coordinate system
(0,0)
(152,92)
(319,199)
320 x 200 game viewport
1
Origin at the top-left corner
2
x grows to the right
3
y grows downward
4
The display is 320 by 240; games draw in a centred 320 by 200 viewport
Notes: The 20-pixel bands above and below the viewport are status bands owned by the runtime.

## Slide 11: The downward y axis
1
A larger y is lower on the display
2
Moving up means subtracting from y
3
Gravity adds to y
4
If something moves the wrong way, check the sign of your y change first
y ↓
the most common early confusion

## Slide 12: RGB565: a pixel in two bytes
1
5 bits red
32 levels, in the top bits of the 16-bit word.
2
6 bits green
64 levels: the eye is most sensitive to green.
3
5 bits blue
32 levels, in the low bits.
Notes: 0xF800 red, 0x07E0 green, 0x001F blue, 0xFFE0 yellow, 0xFFFF white (65535 in decimal).

## Slide 13: Named colours
Constant | RGB565 | Constant | RGB565
PRG32_COLOR_BLACK | 0x0000 | PRG32_COLOR_YELLOW | 0xffe0
PRG32_COLOR_WHITE | 0xffff | PRG32_COLOR_CYAN | 0x07ff
PRG32_COLOR_RED | 0xf800 | PRG32_COLOR_MAGENTA | 0xf81f
PRG32_COLOR_GREEN | 0x07e0 | PRG32_COLOR_BLUE | 0x001f

## Slide 14: Two ways to name a colour
1
Direct: pass an RGB565 value to a drawing call
2
Indexed: set one of 256 palette entries, then draw with the index
3
On the board the framebuffer stores one byte per pixel
4
320 by 200 indices fit in 64,000 bytes of microcontroller RAM
256
palette entries; one byte per pixel

## Slide 15: The drawing calls you will use most
Call | What it does
prg32_gfx_clear(color) | Fill the viewport with one colour
prg32_gfx_pixel(x,y,color) | Set one pixel
prg32_gfx_rect(x,y,w,h,color) | Filled rectangle: the workhorse
prg32_gfx_text8(x,y,s,fg,bg) | A string in 8 by 8 characters
prg32_sprite_hitbox(...) | Non-zero if two rectangles overlap

## Slide 16
02
Input
All the buttons in one integer

## Slide 17: The input bitmask
Constant | Button | Bit
PRG32_BTN_LEFT | left | 0x01
PRG32_BTN_RIGHT | right | 0x02
PRG32_BTN_UP | up | 0x04
PRG32_BTN_DOWN | down | 0x08
PRG32_BTN_A | A | 0x10
PRG32_BTN_B | B | 0x20
PRG32_BTN_START | start / select | 0x40
Notes: Player two uses the same layout shifted into bits 8 to 14.

## Slide 18: Test with AND, never with equality
input & PRG32_BTN_LEFT
True whenever the left bit is set
Other buttons may be held too
This is what you want
input == PRG32_BTN_LEFT
True only if left is the only button
Fails when A is also held
A classic beginner bug
Notes: The bitmask mirrors how hardware presents buttons: as bits in a register.

## Slide 19: Check your understanding
LEFT and A are held. What does prg32_input_read return?
A
0x01
B
0x10
C
0x11
D
0x05
Notes: Answer: C. 0x01 | 0x10 = 0x11.

## Slide 20
03
Sound and cartridges
Events you can hear; games you can ship

## Slide 21: Sound: a note when something happens
1
prg32_audio_note(channel, instrument, note, volume, ms)
2
The note is a MIDI number: 60 is middle C, 69 is A at 440 Hz
3
Eight mixer channels; the call returns at once
4
prg32_buzzer_tone is legacy: silent on the current reference board
5
Trigger sound on events, never every frame

## Slide 22: From source to running game
game.S or game.c
your three functions
RISC-V toolchain
compile and link
.prg32 cartridge
header + code
PRG32 runtime
loads, validates
init / update / draw
your game runs
The firmware is flashed once. Cartridges are then uploaded over Wi-Fi, staged into QEMU, or opened in PRG32-QT.

## Slide 23: Three properties of a cartridge
1
Portable
Calls the runtime through a numbered ABI table (version 1.6, 139 entries), not fixed addresses. Survives firmware updates.
2
Stored in slots
Four persistent slots, cart0 to cart3. One runs at a time; A+B at boot opens setup.
3
Budgeted
64 KiB of executable memory by default; 32 and 128 KiB profiles exist. The build tool checks the limit.

## Slide 24: The two reference targets, concretely
Physical board
ESP32-C6
Build directory build-esp32c6
ILI9341 display, joystick, I2S audio
Cartridges arrive over Wi-Fi
QEMU emulator
ESP32-C3 emulator profile
Build directory build-qemu
Virtual RGB screen, keyboard
Cartridges are staged into flash
Notes: Never flash a build-qemu image to a real board: it targets a display that does not exist there.

## Slide 25
04
Design principles
Rules that separate students who succeed from students who struggle

## Slide 26: Three rules for first games
1
Start with returns
Write init, update, draw so each returns at once. Build. Confirm it runs.
2
One thing at a time
A variable; draw it; move it; a boundary; a collision. Verify each by eye.
3
Sound comes last
A beep at the wrong time is a symptom. Get the visual logic solid first.

## Slide 27: A map of the example games
Example | What it teaches first
pong | State, input, boundaries, one collision
breakout | Arrays of objects, removal on hit
space_invaders | Many moving objects, waves
tetris | A fixed grid, line clears
platformer | Tile flags, gravity, camera
raycaster | Fixed-point arithmetic

## Slide 28: Checkpoint: answer without looking back
1
What are the three functions every PRG32 game provides?
2
In which direction does y grow?
3
How do you test whether one button is pressed?
4
What is a portable cartridge?
5
Why must QEMU and board builds use separate directories?

## Slide 29: Next steps and reading
Before the next session
Chapter 3: install the toolchain and build the firmware
Bring a laptop with 5 GB free
Memorise the three-function contract
Reading and sources
Textbook, Chapter 2
PRG32 docs/software/framework_manual.md
PRG32 docs/software/cartridges.md and abi.md
PRG32 docs/usage/profiles.md