## Slide 1
CHAPTER 5 | LABORATORY | 45 MINUTES
Assembly Lab 1: Hello, Stack Frame, Counter
Build three small cartridges, trace registers by hand and in the debugger, break and repair a stack frame
Audience: computer architecture students (RISC-V assembly track)
Playing with RISC-V: Assembly, C, and Retro Games on the PRG32 Platform
Notes: Teaching support for Chapter 5 of the textbook. Practical, step-by-step session: learners work at their machines; keep each step to its time box. Preparation: Working toolchain (setup lab). PRG32-QT for the tracing steps. Textbook examples folder available on each machine.

## Slide 2: Learning objectives
1
Build and run an assembly cartridge that prints text
2
Trace a load-modify-store sequence by hand and confirm it in a debugger
3
Write a correct prologue and epilogue
4
Add a state variable in .data and change it every frame
5
Diagnose a missing sw and a missing ra save
Notes: State the objectives; return to this slide at the end.

## Slide 3: Plan of the session
9'
8'
9'
12'
7'
1
Print
2
Trace by hand
3
The frame
4
Counter
5
Break and fix
Notes: Total: 45 minutes.

## Slide 4: Working method
1
Predict on paper, then run
2
One change per build
3
Use cartridge summary when a build surprises you
4
Keep a register table: name, value before, value after

## Slide 5
01
Print
A cartridge that writes to the text console

## Slide 6: print_asm.S
.option norelax
.section .text
.global print_init
.global print_update
.global print_draw
print_init:
addi sp, sp, -16 # make 16-byte frame (keep sp 16-aligned)
sw ra, 12(sp) # save return address into the frame
call prg32_console_clear # clear text console (C helper)
la a0, title # put address of string in a0 (1st argument)
call prg32_console_write # print it
lw ra, 12(sp) # restore the return address
addi sp, sp, 16 # tear down the frame
ret # now ret goes to the right place
print_update:
ret
print_draw:
ret
.section .rodata
title:
.asciz "HELLO PRG32\n" # a zero-terminated string
1
init does the work, once
2
The string is zero-terminated: .asciz
3
update and draw only return
Notes: Source: examples/asm_first_contact/print_asm.S

## Slide 7: Build and run print
1
Copy examples/asm_first_contact/print_asm.S to work/print/print.S
2
python3 -m prg32 cartridge build work/print/print.S --portable --entry-prefix print --name print --out work/print/print.prg32
3
python3 -m prg32 qemu upload work/print/print.prg32
4
python3 -m prg32 qemu run
Step 1
about 5 min
Expected result
HELLO PRG32 on the 40 by 25 text console.

## Slide 8: Change the message
1
Change the string to your name
2
Add a second string and a second write
3
Rebuild and run
4
What does \n do? Remove it and observe
Step 2
about 4 min
Expected result
Two lines of text; without \n the second string continues on the same line.

## Slide 9: Check your understanding
Why is the string in .rodata and not in .text?
A
Strings cannot be executed
B
It is data that never changes; sections keep code and data apart
C
.text is full
D
The console requires it
Notes: Answer: B. Read-only data has its own section.

## Slide 10
02
Trace by hand
Be the processor

## Slide 11: The sequence to trace
la t0, hello_x # t0 = ADDRESS of hello_x
lw t1, 0(t0) # t1 = VALUE stored at that address
addi t1, t1, 1 # change the value (in the register)
sw t1, 0(t0) # write the new value back to memory
1
Assume hello_x is at address 0x40800100
2
Assume it currently holds 20
Notes: Source: examples/asm_first_contact/load_modify_store.S

## Slide 12: Fill in the register table
1
Draw a table: instruction, t0 after, t1 after, memory at 0x40800100 after
2
Fill one row per instruction
3
Which row changes memory?
4
Which rows change only registers?
Step 3
about 5 min
Expected result
la: t0 = 0x40800100. lw: t1 = 20. addi: t1 = 21. sw: memory = 21. Only sw changes memory.

## Slide 13: The answer
Instruction | t0 | t1 | Memory
la t0, hello_x | 0x40800100 | ? | 20
lw t1, 0(t0) | 0x40800100 | 20 | 20
addi t1, t1, 1 | 0x40800100 | 21 | 20
sw t1, 0(t0) | 0x40800100 | 21 | 21

## Slide 14: Check your understanding
You delete the sw line. After 100 frames, hello_x holds?
A
120
B
100
C
20
D
21
Notes: Answer: C. The register changed, memory never did.

## Slide 15
03
The frame
Prologue, body, epilogue

## Slide 16: Write a frame from memory
1
Close the book
2
Write the prologue for a function that calls two helpers
3
Write the matching epilogue
4
Compare with print_init
Step 4
about 4 min
Expected result
addi sp, sp, -16 / sw ra, 12(sp) ... lw ra, 12(sp) / addi sp, sp, 16 / ret.

## Slide 17: Watch ra in the debugger
1
Import print.prg32 into PRG32-QT in debug mode
2
Select Init, set a breakpoint on its first instruction, reset the cartridge
3
Step: note sp after the addi
4
Step over the first call: note how ra changed
Step 5
about 6 min
Expected result
sp decreases by 16. After the call returns, ra holds an address inside print_init, not the framework's.

## Slide 18: What you just saw
1
The prologue saved the framework's return address in memory
2
The call replaced ra with an address inside your function
3
The epilogue put the original back
4
ret then returned to the framework, not to yourself

## Slide 19
04
Counter
State that changes every frame

## Slide 20: Start the counter cartridge
1
Create work/counter/counter.S
2
Declare 'counter: .word 0' in .data and a title in .rodata
3
Write counter_init, counter_update, counter_draw that only return
4
Build with --entry-prefix counter and run
Step 6
about 5 min
Expected result
A blank cartridge that builds and runs. The skeleton first, always.

## Slide 21: counter_update
counter_update:
addi sp, sp, -16
sw ra, 12(sp) # save return address
la t0, counter
lw t1, 0(t0)
addi t1, t1, 1 # count one tick per frame
sw t1, 0(t0)
lw ra, 12(sp) # load return address
addi sp, sp, 16
1
Type this into your file
2
Say each line aloud: load, modify, store
Notes: Source: examples/asm_first_contact/counter.S

## Slide 22: counter_draw
counter_draw:
addi sp, sp, -16
sw ra, 12(sp) # save return address
call prg32_console_clear
la a0, title
call prg32_console_write
la t0, counter
lw a0, 0(t0)
call prg32_console_hex32 # print numeric value
lw ra, 12(sp)
1
Clear, write the title
2
Load counter into a0: it is the argument
3
hex32 prints a0 in hexadecimal
Notes: Source: examples/asm_first_contact/counter.S

## Slide 23: Run the counter
1
Add update and draw to your file
2
Rebuild, stage, run
3
Time ten seconds: how much did the counter grow?
4
Compute frames per second from your reading
Step 7
about 6 min
Expected result
A hexadecimal number that increases steadily, about 0x12C (300) per ten seconds at 30 frames per second.

## Slide 24: Count by two; count down
1
Change the increment to 2 and predict the new rate
2
Change it to -1: what does the display show after zero?
3
Explain 0xFFFFFFFF
Step 8
about 4 min
Expected result
The rate doubles. Counting down from 0 shows 0xFFFFFFFF: -1 in two's complement.

## Slide 25
05
Break and fix
Learn the symptoms now, while you know the cause

## Slide 26: Bug 1: the missing store
1
Comment out the sw in counter_update
2
Predict the display
3
Run and confirm
4
Restore the line
Step 9
about 3 min
Expected result
The counter stays at zero: the incremented value never leaves the register.

## Slide 27: Bug 2: the unsaved ra
1
Comment out 'sw ra' and 'lw ra' in counter_draw
2
Predict what happens
3
Run; then look at pc in PRG32-QT
4
Restore the lines
Step 10
about 4 min
Expected result
The cartridge hangs: draw returns into itself. In the debugger pc circles inside counter_draw.

## Slide 28: Bug 3: the unbalanced stack
1
Change the epilogue's 'addi sp, sp, 16' to 'addi sp, sp, 8'
2
Run in PRG32-QT and watch sp each frame
3
Restore the line
Step 11
about 3 min
Expected result
sp creeps downward 8 bytes per frame: a stack leak that eventually corrupts memory.

## Slide 29: You can now
1
Build and run an assembly cartridge
2
Trace load-modify-store by hand
3
Write a stack frame without looking
4
Keep state in .data and change it per frame
5
Recognise a missing store, an unsaved ra, and a stack leak

## Slide 30: Next steps and reading
Before the next session
Keep counter.S: the next lab adds input to it
Read Chapter 6
Write up Bug 2 with the pc values you observed
Reading and sources
Textbook, Chapter 5
PRG32 docs/learn/labs/lab_01_hello_world.md
PRG32 docs/learn/labs/debugging_register_tracing.md